## Slide 1: Solid waste manegement

## Slide 2: Solid Waste management
is the collection, transport, processing, recycling or disposal, and monitoring of waste materials

## Slide 3: Landfill
Disposing of waste in a landfill involves burying the waste, and this remains a common practice in most countries
A properly designed and well-managed landfill can be a hygienic and relatively inexpensive method of disposing of waste materials

## Slide 4
common byproduct of landfills is gas (mostly composed of methane and carbon dioxide), which is produced as organic waste breaks down anaerobically. This gas can create odour problems, kill surface vegetation, and is a greenhouse gas.
Deposited waste is normally compacted to increase its density and stability, and covered to prevent attracting vermin (such as mice or rats).

## Slide 5
Many landfills also have landfill gas extraction systems installed to extract the landfill gas.
Gas is pumped out of the landfill using perforated pipes and flared off or burnt in a gas engine to generate electricity.

## Slide 7: Incineration
Incineration and other high temperature waste treatment systems are sometimes described as "thermal treatment".
Incineration is a disposal method in which solid organic wastes are subjected to combustion so as to convert them into residue and gaseous products

## Slide 8
This method is useful for disposal of residue of both solid waste management and solid residue from waste water management
This process reduces the volumes of solid waste to 20 to 30 percent of the original volume.
Incinerators convert waste materials into heat, gas, steam and ash.

## Slide 9
It is recognized as a practical method of disposing of certain hazardous waste materials (such as biological medical waste
Incineration is a controversial method of waste disposal, due to issues such as emission of gaseous pollutants.

## Slide 10
Particular concern has focused on some very persistent organics such as dioxins which may be created within the incinerator and may have serious environmental consequences in the area immediately around the incinerator.
On the other hand this method produces heat that can be used as energy
Incineration is common in countries such as Japan where land is more scarce, as these facilities generally do not require as much area as landfills.

## Slide 11: Recycling
The popular meaning of ‘recycling’ in most developed countries refers to the widespread collection and reuse of everyday waste materials such as empty beverage containers
These are collected and sorted so that the raw materials from which the items are made can be reprocessed into new products

## Slide 12
Material for recycling may be collected separately from general waste using dedicated bins and collection vehicles
The most common consumer products recycled include aluminum such as beverage cans, copper such as wire and aerosol cans glass bottles and jars magazines and news papers