## Slide 1: Spectrophotometric Methods For Determination Of Proteins
Experiment 2

## Slide 2
To Learn Different Method Of proteins determination
In this Lab you will using the following spectrophotometric methods:
Bradford Method.
Chemical reagents are added to the protein solutions to develop a color whose intensity is measured in a spectrophotometer.
2. Warburg-Christian Method ( A280/ A260 Method).
Relies on direct spectrophotometric measurement
Objectives

## Slide 3: Important Terms
Qualitative assays
Determine if specific substance is there or not, by color or some other quality
Quantitative assays Determine the concentration of a substance
Assays
Sensitivity of an assay is a measure of how little of the analyte the method can detect
Specificity of an assay relates to how good the assay is in discriminating between the requested analyte and interfering substances
Specifity and sensivity

## Slide 4: Importance of determining concentration of protein
Protein assays are one of the most widely used methods in life science research.
Estimation of protein concentration is necessary cell biology, molecular biology and other research applications.
Is necessary before processing protein samples for isolation, protein purification, separation and analysis.

## Slide 5
Spectrophotometric and colorimetric methods
Acid hydrolyse a portion of the sample
The determination of protein concentration
Used for routine estimation, most of them are colometric
Where a portion of the protein solution is reacted with a reagent that produces a coloured product.
However, none of these methods is absolute,
And then carry out amino acid analysis on the hydrolysate
A truly accurate method
However, this is expensive and relatively time-consuming, particularly if multiple samples are to be analysed.

## Slide 6: Spectrophotometric method for determining the protein concentration
Bicinchoninic acid method
lowry
Bradford
Warburg christian
(A280/A260)
There are a wide variety of protein assays available. but each assay has its own advantages and limitations
The factors that you should consider to choose Method :
Sensitivity
The presence of interfering substance
Time available of the assay
Cost

## Slide 7: 1-Bicinchoninic acid method
In general, this method has a high sensitivity (1 µg )
Principle:
Cu+2 form a complex with nitrogen of the peptide bond under alkaline conditions producing cu+(the Cu++ was reduced to Cu+)
This cu+ will then chelated by BCA to produce a copper-BCA complex with maximum absorbance 562 nm
Alkaline condition

## Slide 8
STEP 1. (A)
STEP 2. (B)
Cu+2
Cu+
Cu+
Reduction
Figure-1: BCA Method

## Slide 9: 2-Bradford assay
Fast, accurate and high sensitivity [1 μg protein can be detected].
The method is recommended for general use, especially for determining protein content of cell fractions and assessing protein concentrations for gel electrophoresis, about 1- 20 μg protein for micro assay or 20-200μg protein for macro assay.
Principle:
Generally, Coomessie brilliant blue G-250 bind to protein (binds particularly to basic and aromatic amino acids residues ) in acidic solution
Make a complex which will shift the wavelength of maximum absorbance (λmax) 465 to 595 nm.
Cell fractionation

## Slide 10: 2-Bradford assay
How it happened?
Coomessie brilliant blue G-250 dye exists in three forms: cationic (red), neutral (green), and anionic (blue)
Under acidic conditions, the dye is predominantly in the doubly protonated red cationic form (Amax = 470 nm).
However, when the dye binds to protein, it is converted to a stable unprotonated blue form (Amax = 595 nm) It is this blue protein-dye form that is detected at 595 nm
This complex stabilized by hydrophobic and ionic interaction

## Slide 11
Bradford reagent alone –maximum absorbance at (465 nm)
Bradford assay
Bradford reagent and protein maximum absorbance at (595 nm)

## Slide 12
Concentration (µg/ml) | Unknown | Distilled Water | Bovine Serum Albumin(BSA) (150µg/ml) | Tube
Blank | - | 1 ml | - | (blank)
10.5 | - | 0.93 ml | 0.07 ml | A
19.5 | - | 0.87 ml | 0.13 ml | B
39 | - | 0.74 ml | 0.26 ml | C
60 | - | 0.6 ml | 0.4 ml | D
99 | - | 0.34 ml | 0.66 ml | E
150 | - | - | 1 ml | F
? | 1 ml | - | - | G
? | 1 ml | - | - | H
A- Set up 9 tubes and label them as follows:
Add 5ml of Bradford reagent to each tube [blank – H].
C- Mix and Incubate at room temperature for 5 min.
D- Measure the absorbance at 595 nm.
Bradford assay-Method

## Slide 13
Absorbance at 595 nm | Concentration (µg/ml) | Tube
 | Blank | (blank)
 | 10.5 | A
 | 19.5 | B
 | 39 | C
 | 60 | D
 | 99 | E
 | 150 | F
 | =.................. | G
 | =.................. | H
Bradford assay-Results

## Slide 14: 3-Warburg christian (A280/A260)
Relies on direct spectrophotometric measurement.
Fast
Semiquantitative analysis
Principle:
Proteins can absorb light at 280 ultraviolet
This is because proteins contains aromatic amino acids tyrosine and tryptophan give proteins .
The amount of these residues vary greatly from protein to protein so this method is semiquantitave

## Slide 15
Nucleic acid interfere with this method.
So to solve this problem, we will measure the absorbance at 280 then we measure at 260
Calculate A280/A260 ratio,
then from a specific table we can get the correction factor
Concentration=A280 x correction factor
Or by another way:
[groves formula]:
Protein concentration [mg/ml]=[1.55 X A280]-[0.76 X A260]
Warburg christian (A280/A260)

## Slide 16
-Calculate the protein concentration in the unknown from the following equations:
A280 =…………………
A260 =…………………
A280/ A260 =…………………
Correction factor =…………………
A280 x correction factor =……… mg/ml protein
Unknown concentration =………………… mg/ml
2-or [groves formula]:
Protein concentration [mg/ml]=[1.55 X A280]-[0.76 X A260]
Warburg christian (A280/A260)

## Slide 17
-A protein solution that has a low A280/A260 ratio: Highly contaminated by DNA.
[It shows a higher absorbance at 260nm comparing to absorbance at 280nm].
-A protein solution that has a high A280/A260 ratio: Less contaminated by DNA.
[It shows a lower absorbance at 260nm comparing to absorbance at 280nm].
Warburg christian (A280/A260)

## Slide 18: Summary
ASSAY | ABSORPTION | MECHANISM | reagent
UV absorption | 280 nm | Tyrosine and tryptophan absorption | No reagent
Bicinchoninic acid | 562 nm | copper reduction (Cu2+ to Cu1+), BCA reaction with Cu1+ | BCA
Bradford or Coomassie brilliant blue | 595 nm | complex formation between Coomassie brilliant blue dye and proteins | Coomassie brilliant blue
Protein assay is important in many aspects
There are Many Methods for protein determination, each had it own advantages and disadvantages

## Slide 19: References
Principles and Techniques of Biochemistry and Molecular Biology
Quick Start™ Bradford Protein Assay Instruction Manual