## Slide 1: Spectrophotometry

## Slide 2: Coupled Assay
Many compounds of biological importance do not have a distinct absorption maximum λmax . Nevertheless, their concentration can be determined if they can be linked to or coupled with a reaction that fulfills the following conditions :
1- The reaction they are coupled or linked to should be a reaction that produces or allows the production of a substance that has a characteristic absorption peak .
2- The reaction they are coupled or linked to should allow a stoichiometrical production of
In coupled assay reactions the product of the first reaction is the substrate of the following reaction ;
A + B ------------> C + D ------------> E + F
A = substance under study that does not have a distinct λmax .
F = has a distinct λmax .
Thus A can be estimated by measuring the absorbance of F .
Example : To 2.0ml of a glucose solution 1.0ml of a solution containing excess ATP , NADP+ , MgCl2 , hexokinase and Glucose -6-phosphate dehydrogenase was added . Calculate the concentration of glucose in the original solution. Absorbance at 340nm of NADPH = 0.91, am= 6220
The following are the reactions taking place ;
Glucose + ATP glucose -6-phosphate + ADP

## Slide 3: Coupled Assay
Glucose -6-phosphate + NADP+ 6-phosphogluconate +
NADPH+ H+
Glucose has no absorbtion at 340nm , but NADPH does , and from reaction 1 mole of glucose produces 1 mole of NADPH , thus each mole of NADPH produced originates from 1 mole of glucose in the original solution .
Absorbance at 340nm is the absorbance of NADPH = 0.91
A = am x C x 1 = 0.91 = 6220 x C x 1
C NADPH = 0.91 / 6220 = 1.46x10-4 M .
Thus there is 1.46 x 10-4 M of glucose present in the test solution .
The glucose concentration in the original solution = 1.46 x 10-4 x 3/2 = 2.2 x 10-4 M

## Slide 4: Coupled Assay
Glucose has no absorbtion at 340nm , but NADPH does , and from reaction 1 mole of glucose produces 1 mole of NADPH , thus each mole of NADPH produced originates from 1 mole of glucose in the original solution .
Absorbance at 340nm is the absorbance of NADPH = 0.91
A = am x C x 1 = 0.91 = 6220 x C x 1
C NADPH = 0.91 / 6220 = 1.46x10-4 M .
Thus there is 1.46 x 10-4 M of glucose present in the test solution .
The glucose concentration in the original solution = 1.46 x 10-4 x 3/2 = 2.2 x 10-4 M

## Slide 5: Problems
Calculate the absorbance and the transmission at 260nm and 340nm of the following solutions in a 1cm cuvette . a) 2.2 x10-5 M NADH
b) 7 x 10-6 M NADH plus 4.2 x 10-5 M ATP .
This solution contains one absorbing substance ( NADH).
A260 = am x C x l = 15000 x (2.2 x10-5 ) x 1 = 0.33
A = Log I° / I , thus 0.33 = log 1.0 – log I ,
0.33 = - log I , I = antilog – 0.33 = 0.464 .
Absorbance and transmission at 340nm,
A = 6220 x 2.2 x10-5 x1 = 0.1368
A = Log I° / I , thus 0.1368 = log 1.0 – log I
am |  | 
Compound | 260nm | 340nm
NADH | 15000 | 6220
ATP | 15400 | 0.0

## Slide 6: Problems
0.1368 = -log I , so I = antilog -0.1368
I = 0.729.
b) The solution contains two absorbing substances ,
At 260nm
A = ANADH + A ATP
ANADH = 15000 x (7 x 10-6 ) x1 = 0.105
A ATP = 15400 x (4.2 x 10-5 ) x 1 = 0.646
A Total = 0.105 + 0.646 = 0.751
A= Log I° / I = 0.751 = log 1.0 –log I
0.751 = -log I , so I = antilog - 0.751
I = 0.177 .
At 340nm only NADH absorbs .
A = 6220 x (7 x 10-6 ) x1 = 0.043
A= Log I° / I = 0.043 = log 1.0 –log I , so I = antilog - 0. 043
I = 0.905 .

## Slide 7: Problems
Calculate the concentration of ATP and NADPH in solutions with absorbance's ,
a) 0.15 at 340nm and 0.9 at 260nm .
b) Zero at 340nm and 0.750 at 260nm .
c)0.22 at 340nm and 0.531 at 260nm .
Since this solution contains two absorbing substances , thus we will start with absorbance at 340nm since only NADPH absorbs .
A 340nm = A NADPH only .
A = am x C x l = 6220 x C x 1
C = 0.15 / 6220 = 2.4 x 10-5 M
am |  | 
Compound | 260nm | 340nm
NADPH | 15000 | 6220
ATP | 15400 | 0.0

## Slide 8: Problems
A260nm = A ATP + A NADPH
A NADPH = am x C x l = 15000 x 2.4 x 10-5 x1 = 0.36
A ATP = A Total - A NADPH = 0.9 – 0.36 = 0.54
A ATP = am x C x l = 0.54 = 15400 x C x1
C = 0.54 / 15400 = 3.5 x 10-5 M
b) Since Absorbance at 340nm is zero , and NADPH is the only absorbing substance at that wavelength thus the concentration of NADPH is zero .
Accordingly the absorbance 0.75 at 260nm is the absorbance of ATP only .
A ATP = am x C x l
C ATP = 0.751 / 15400 = 4.8x10-5 M .
c) At 340nm only NADPH absorbs .
0.22 = 6220 x C x1
CNADPH = 0.22/ 6220 = 3.5 x10-5 M .

## Slide 9: Problems
At 260nm both ATP and NADPH absorb ,
Thus A = A ATP + A NADPH
A NADPH = 15000 x ( 3.5 x 10-5 ) x1 = 0.53
Since A NADPH = ATotal
Thus ATP concentration must be Zero .