## Slide 1: Classful Subnetting IPv4
References:
  CCNA Curriculum
  CCNA Command Quick Reference by Scott Epson

## Slide 2: Revision: Converting Decimal To Binary
Example convert the decimal number 198 to binary number?
Decimal Number | Divisor | Reminder
198 | 2 | 0
99 | 2 | 1
49 | 2 | 1
24 | 2 | 0
12 | 2 | 0
6 | 2 | 0
3 | 2 | 1
1 | 2 | 1
0 |  | 
The binary number is the reminder written from the bottom to the top
Decimal: 198
Binary: 11000110

## Slide 3: Revision: Converting Binary To Decimal
Converting the binary number 11000110 to decimal number
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
+ 0 x 20 | + 1 x 21 | + 1 x 22 | + 0 x 23 | + 0 x 24 | + 0 x 25 | + 1 x 26 | 1 x 27
0 | 2 + | 4 + | 0 + | 0 + | 0 + | 64 + | 128 +
 |  |  |  | = 198 | Number | Decimal | 

## Slide 4: IP Classes
Class A
Class B
Class C

## Slide 5: Host & Network Portions for the different classes
Class | First octet | Example | Network Part | Host part | Number of Networks | Number of Hosts *
A | 1-126 | 12.240.60.89 127.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 126 | (23*23*23)-2 = 16777214
B | 128-191 | 130.240.60.89 191.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 16,384 | (23*23)-2 = 65,534
C | 192-223 | 192.240.60.89 223.8.90.2 | xxx.xxx.xxx.xxx | xxx.xxx.xxx.xxx | 2 million | (23)-2 = 254
The first address ( xxx.xxx.xxx.0) & the last address (xxx.xxx.xxx.111) are reserved for the network
( xxx.xxx.xxx.0) for the network & (xxx.xxx.xxx.111) for broadcasting

## Slide 6: Example1
Network Address: 72.0.0.0
Host1: 72.167.98.77
Host2: 72.167.98.70
Host3: 72.167.98.75
Host4: 72.167.98.71
What is the Network address?
72.0.0.0
To which class this network belongs?
Class A because network number = 72
72 ϵ {1-126}
What is the broadcast address?
72.255.255.255
What is the IP addresses of the hosts?
IP Address of host1: 72.167.98.77
IP Address of host2: 72.167.98.70
IP Address of host3: 72.167.98.75
IP Address of host4: 72.167.98.71
LAN

## Slide 7: What is subnetting?
Subnetting is the process of borrowing bits from the HOST bits, in order to divide the larger network into small subnets.
Subnetting does NOT give you more hosts, but actually costs you hosts (decrease number of hosts).
You lose two host IP Addresses for each subnet, and perhaps one for the subnet IP address and one for the subnet broadcast IP address.

## Slide 8: Why Do We Use Subnetting?
A company uses two or more types of LAN technology (for example, Ethernet, Token Ring) on their network or different physical media (such as Ethernet, FDDI, WAN, etc.)
Two network segments are restricted by distance limitations (for example, remote offices linked via point-to-point circuit).
Segments need to be localized for network management reasons (accounting segment, sales segment, etc.).
Hosts which dominate most of the LAN bandwidth need to be isolated.
Security.
The most common reason is to control network traffic.

## Slide 9: How it works?
The IP address is split into a network and host portion.
The network portion always remains fixed for a particular network, while the remaining bits which make up the host portion can be altered to give the range of addresses to assign to hosts.
To determine where the network portion ends and the host portion begins, a subnet mask is used.

## Slide 10: Example (1)
Given the following IP address 38.9.211.19 with a subnet mask of 255.255.255.240 determine:
  Network Address
  Default subnet mask
  Broadcast address of the network
  Subnet ID
  Broadcast address of the subnet.
  First & last host address in the subnet.

## Slide 11: Example (1)
Network Address
    To determine the network address we have to determine the class of the IP address
    38.9.211.0  38 ϵ {1-126} Class A
    In class A network portion is the first octet & the remaining three octets for the host are zeros.
    Network Address: 38.0.0.0

## Slide 12: Example (1)
  Default subnet mask
  For Class A addresses, default subnet mask is: 255.0.0.0
  Broadcast address of the network
  Changing all the host bits to 1 give you the broad cast address:
  Broadcast Address = 38.255.255.255

## Slide 13: Example (1)
  Subnet ID:
    First: Determine the following bits in the following order:
      Network portion (N) (Fixed depends on the IP class)
      Subnet portion (S) (From the end of the network portion to the last bit in the mask with the value 1)
      Host portion (H) (The remaining bits after the subnet portion)
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
N = 8
H=4
S = 20

## Slide 14: Example (1)
    Second:
    Do the AND operation between the IP address & the mask
IP 00100110.00001001.11010011 . 00010011
Mask 11111111 . 11111111 . 11111111 .11110000
    ______________________________________________
  Subnet ID 00100110.00001001.11010011 . 00010000
  Subnet ID in decimal = 38.9.211.16
AND

## Slide 15: Example (1)
  Broadcast address of the subnet.
  To get the broad cast address replace the host bits in the subnet ID with 1s
  Subnet ID 00100110.00001001.11010011 . 00010000
Broadcast Address 00100110.00001001.11010011 . 00011111
Broadcast Address in decimal 38.9.211.31
Host bits

## Slide 16: Example (1)
  First & last host address in the subnet.
  To get the first address replace all the host bits with zeros except the last bit replace it with one as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  First Host Address 00100110.00001001.11010011 . 00010001
  First Host Address in decimal 38.9.211.17
Host bits
Host bits

## Slide 17: Example (1)
  First & last host address in the subnet.
  To get the last address replace all the host bits with ones except the last bit replace it with zero as follows:
  Subnet ID 00100110.00001001.11010011 . 00010000
  Last Host Address 00100110.00001001.11010011 . 00011110
  Last Host Address in decimal 38.9.211.30
Host bits
Host bits

## Slide 18: Example (2): IP=182.250.200.028, SM= 255.255.255.248
  IP = 10110110. 11111010.11001000.00011100
  SM = 11111111.11111111.11111111.11111000
  Class of the IP is B
  Network Address= 10110110. 11111010.00000000.00000000
  Default Subnet Mask of the IP = 11111111.11111111.00000000.00000000
  Broadcast address of the network = 10110110. 11111010.11111111.11111111
  Subnet ID = 10110110. 11111010.11001000.00011000
  Broadcast address of the subnet = 10110110. 11111010.11001000.00011111
  First IP address = 10110110. 11111010.11001000. 00011001
  Last IP address = 10110110. 11111010.11001000. 00011110
N = 16
SN = 13
H= 3

## Slide 19: In Decimal Example (2): IP=182.250.200.28, SM= 255.255.255.248
  IP = 182.250.200.28
  SM = 255.255.255.248
  Class of the IP is B
  Network Address= 182.250.0.0
  Default Subnet Mask of the IP = 255.255.0.0
  Broadcast address of the network = 182.250.255.255
  Subnet ID = 182.250.200.024
  Broadcast address of the subnet = 182.250.200.31
  First IP address = 182.250.200.025
  Last IP address = 182.250.200.030

## Slide 20: Demonstrating the different type of IPs in Example (2)
Subnet ID: 182.250.200.024
Network Address: 182.250.0.0
First IP: 182.250.200.025
Last IP: 182.250.200.030

## Slide 21: Public and private IP addresses
Public IP addresses are unique and it must be obtained from an Internet service provider (ISP)
RFC 1918 sets aside three blocks of IP addresses for private, internal use. These three blocks consist of one Class A, a range of Class B addresses, and a range of Class C addresses. Addresses that fall within these ranges are not routed on the Internet backbone. Internet routers immediately discard private addresses.

## Slide 22: Public and private IP addresses
If addressing a nonpublic intranet, a test lab, or a home network, private addresses can be used instead of globally unique addresses.
Connecting a network using private addresses to the Internet requires translation of the private addresses to public addresses. This translation process is referred to as Network Address Translation (NAT).