## Slide 1: Tablets Excipients
Notes: <number>

## Slide 2: Their role: To ensure that tablets of specified quality are prepared. The common types of tablet’s excipients are described in the figure.
Notes: <number>

## Slide 3: In addition to the drug, tablets contain a number of inert materials, known as additives or excipients. They are classified according to the part they play in the finished tablet. 1- The first group contains excipients that help in imparting satisfactory compression characteristics to the formulation. These include; diluents, binders glidants and lubricants. 2- The second group helps to give additional desirable physical characteristics to the finished tablet. These include; disintegrants, coloring, flavoring and sweetening agents.
Notes: <number>

## Slide 4: A typical tablet contains
Notes: <number>

## Slide 5: Tablet excipients • Filler (or diluent): A filler, such lactose, is included to increase the size of the tablet. This is necessary as often the amount of 'active ingredient' is so tiny that the tablet would be too small to handle without it. • Binder: A binder, such as starch paste or HPMC, is added to hold the tablet together after it has been compressed, stopping it from breaking down into its separate ingredients. • Disintegrant: Disintegrants, such as starch help the tablet to break down into small fragments, when it is ingested. This helps the medicine to dissolve and be taken up by the body so that it can act more quickly. • Glidant: The glidants improve the flowability of the tablet granules or powder by reducing the friction between particles, preventing formation of lumps. • Antiadherent: The antiadherents stop the powder from sticking to the equipment as the tablet is being made. • Lubricant: Lubricants ensure that the tablet has a smooth surface, they reduce the friction occurs between the walls of the tablets and the walls of the die cavity when the tablet is ejected. • Flavor: Flavoring agents help to make the tablet taste better. • Colorant: Colors are added to help you to recognize your tablet and to make it easier to take your medicine correctly.
Notes: <number>

## Slide 6: I-Diluent (filler or bulking agent): Diluent adds bulk to make the tablet with practical size for compression and to be easily handled. Tablets weigh normally at least 50 mg, therefore a low dose of a potent drugs requires addition of a filler to increase the bulk volume of the powder and hence the size of the tablet. Examples for potent drugs are:
Corticosteroid drugs such as;
Dexamethasone (0.5 mg/Tablet)
Drugs used to replace thyroid hormone
Levothroid Tablet (0.05 mg/Tablet)
Notes: <number>

## Slide 7: • Requirements for a good filler: 1. Chemically inert, biocompatible, cheap. 2. Non-hygroscopic. 3. Good biopharmaceutical properties. (water soluble or hydrophilic). 4. Good technical properties (compactability ) 5. Have an acceptable taste.
Notes: <number>

## Slide 8:  Filler is not necessary if the dose of the drug is high.  Tablet fillers are mainly carbohydrates and celluloses, but also some inorganic salts are used.  One or more diluents may be used in one tablet preparation.
Most common fillers in tablets:
1. Lactose
2. Sugar and sugar alcohol (glucose, sucrose, sorbitol and mannitol.
3. Cellulose and microcrystalline cellulose.
4. Dicalcium phosphate dihydrate.
Notes: <number>

## Slide 9: 1- Carbohydrate fillers Lactose possesses many good filler properties: - It dissolves readily in water. - It has pleasant taste (additional sweetening property). - It is non-hygroscopic and readily dries after wet granulation. - It shows good compressibility. - Fairly non-reactive. - It has high melting point so it does not soften by frictional force of compression. Other sugars or sugar alcohols are sucrose, glucose, sorbitol and mannitol have been used as alternative fillers to lactose, primarily in Lozenges or Chewable tablets because of their pleasant taste. Sucrose: - It provides additional sweetness. - It is somewhat hygroscopic, tends to turn brown in contact with acidic or basic substances.
Notes: <number>

## Slide 10: Mannitol:  It is particularly used as filler for Chewable tablets.  It has a negative heat of solution and imparts a cooling sensation when sucked or chewed. Less sensitive to humidity.  Starches derived from wheat, corn, rice and potato play an important role as diluent, binder and disintegrant.  Exists in a number of polymorphic forms. Sorbitol:  Exists in a number of polymorphic crystalline forms and amorphous form.  Widely used in sugar free mints and as a vehicle in chewable tablets.  Coal taste and good mouth feel.  forms a hard compact.
Notes: <number>

## Slide 11: 2- Celluloses as fillers - They are biocompatible, chemically inert and they have good tablet forming and disintegration properties. - They are also used as dry binders and disintegrants in tablet manufacture. - The most common type of cellulose powder is Microcrystalline cellulose (MCC). Trade names for MCC are Avicel®, Ambicel® and Flocel®. 3- Inorganic salts as fillers: - An important example is Dicalcium phosphate hydrate; it is water insoluble, non-hygroscopic, but hydrophilic i.e. easily wetted by water. It is inexpensive and possesses a high degree of physical and chemical stability. - Calcium phosphates are highly alkaline and thus be incompatible with drug sensitive to alkaline conditions.
Notes: <number>

## Slide 12: Selection of diluent Based on the experience of the manufacturer as well as on the cost of the diluent and its compatibility with the other tablet ingredients, the proper diluent could be chosen. 1- Calcium salts can not be used as fillers for Tetracycline products because calcium interferes with the absorption of Tetracycline from GIT. 2- When drug shows low water solubility, it is recommended that water soluble diluents be used to avoid possible bioavailability problems. 3- The combination of amine bases and salts with Lactose in presence of alkaline lubricant results in discoloration upon ageing.
Notes: <number>

## Slide 13: II- Binder (adhesive): Binder is added to drug-filler mixture. - To promote cohesive compacts during direct compression and ensure the tablet remaining intact after compression. - To promote granulation (i.e. as granulator) to ensure free flowing properties of the particles. - Binders are used either in a solution or in a dry form depending on other materials in the formulation & the method of preparation. The binding action is more effective when the binder is in a solution form than if it was dispersed in a dry form and moisten with the solvent. - Materials commonly used as binders include starch, gelatin and sugars as glucose, lactose. Natural and synthetic gums include acacia, sodium alginate, methylcellulose and carboxymethylcellulose.
Notes: <number>

## Slide 14: Examples for binders
Common traditional solution binders are:
- 10-20% aqueous corn
- 25-50% solution of glucose
- Sucrose
- Molasses
- 10-20% solution of gelatin, freshly prepared and used while warm.
- Natural gums (e.g. acacia)
- Ethylcellulose 5% solution (insoluble in water but dissolved in alcohol or as dry binder), it is widely used as a binder for moisture sensitive materials.
Starch paste
It is prepared by dispersing corn starch in cold purified water to make a 10% w/w solution, followed by warming in a water bath with continuous stirring until a translucent paste is formed. Starch paste is not only useful as a binder, but also as a disintegrant; as during paste formation, not all the starch is hydrolyzed.
Notes: <number>

## Slide 15: More recently used binders today, with improved adhesive properties, are polymers such as polyvinyl pyrrolidone (PVP) and cellulose derivatives e.g. methyl cellulose, Carboxymethyl cellulose (CMC) and the most popular hydroxypropyl methylcellulose (HPMC). HPMC HPMC is more dispersible in hot water and more soluble in cold water, hence in order to obtain smooth gel free from lumps, it is necessary to disperse HPMC first in hot (almost boiling) water, with agitation, followed by sudden cooling. Important examples for dry binders are microcrystalline cellulose (MCC) and cross-linked PVP.
Notes: <number>

## Slide 16: III- Disintegrant: Disintegrant is added to tablet formulation: - To facilitate tablet disintegration (break up) when it contacts fluids in the GIT and thus promotes rapid drug dissolution. - Substances routinely included in tablet formulations and in many hard shell capsule formulation. To promote moisture penetration and dispersion of the matrix of the dosage form in dissolution fluids to expose primary drug particles.
Tablet disintegration
Notes: <number>

## Slide 17
Notes: <number>

## Slide 18: Tablet disintegration may be critical to subsequent drug dissolution rate and to satisfactory bioavailability
Intact tablet
Disintegration
in the GIT
Deaggregation
in the GIT
Granules
Primary drug particles
Drug dissolution
Drug in solution in GIT fluids
Absorption
Drug in blood
Notes: <number>

## Slide 19: Mechanisms of action of disintegrants:
All disintegrants are hygroscopic and drow fluids into the matrix
Two main mechanisms:
1- Facilitate water uptake:
They act by facilitating the transport of fluids (GIT) into the tablet pores, so that the tablet will break into fragments, an obvious example is surface active agent that makes the drug surface very hydrophilic
and thus promote the wetting of the solid followed by penetration into the pores. (An example is Sod. Lauryl Sulphate).
Other substances e.g. starch may promote fluid penetration by capillary forces to suck water into the tablet; the spherical shape of the starch grains increases the porosity of the tablet, thus promoting the capillary action.
Notes: <number>

## Slide 20: 2- Rupture the tablet: Tablet rupturing can be caused by swelling of the disintegrant particles during absorption of fluids (in the GIT).
Dry starch
Starch after exposure to moisture
Notes: <number>

## Slide 21: Examples for disintegrants
Common disintegrants include:
- Starch and its derivatives (Sodium Starch Glycolate).
- Cellulose and its derivatives ( MCC, Sod CMC and Croscaramelose)
- Clays (Veegum, bentonite)
- Alginates
- Cation exchange resin
1- The most traditional disintegrant in conventional tablet is Starch (e.g. potato, maize and corn starch).
Its concentration as disintegrant is up to 10%. They swell in water causing tablet rupturing. Starch in combination with SLS is an effective disintegrant.
2- Super-disintegrants; they can swell dramatically upon exposure to water and thus quickly and effectively break the tablet. They are included in the formulation at relatively low concentration 1-5% by weight. Examples are:
- modified starch (e.g. Sodium Starch Glycolate that swells 7-12 fold in less than 30 sec).
- modified cellulose (e.g. Croscaramelose that swells 4-8 fold in less than 10 sec).
Notes: <number>

## Slide 22
- Cross-linked polyvinylpyrrolidone has been described as having
superiority over corn starch for a number of tablet formulations.
- Veegum has been shown to be more effective as disintegrator in sulfathiazole tablets when most of the quantity is added after granulation and only a small amount before granulation.

## Slide 23: How is disintegrant added during the tablet manufacturing?
Extragranular addition | Intragranular addition | Both Intragranular and Extragranular addition
- It is more common for the disintegrant to be mixed with the dry granules before tablet compression -This procedure will contribute to an effective disintegration of the tablet into small fragments | -Disintegrant can be mixed with other ingredients prior to granulation and thus incorporated into the granules | - Disintegrant may also be added in two steps: A portion is added to drug diluent mixture (Intragranular addition) and the other portion is mixed with the dry granules before compression (Extragranular addition). Double disintegration of tablet.
Notes: <number>

## Slide 24: IV- Glidants, antiadherents and lubricants
They have overlapping functions:
A- Glidants promote the flow of the tablet granules or powder by reducing friction between particles, e.g. colloidal silica.
B- Antiadherents reduce sticking or adhesion of the tablet granules or powders to the faces of the punches or the die walls, e.g. Mg stearate, talc and starch.
C- Lubricants reduce the friction occurs between the walls of the tablets and the walls of the die cavity when the tablet is ejected, e.g. Mg stearate, waxes and talc.
Notes: <number>

## Slide 25: A.Glidants: - They are used in the formulation for direct compression. - They are also added to the granules before tableting to ensure proper flowability of the tablet mass for high production speed.
Examples for glidants:
-Traditional glidant is Talc powder (1-2% by weight).
-The most common glidant today is colloidal silica (AEROSIL) 0.2% by weight.
-Silica particles are very fine so they adhere to the surfaces of other ingredients and improve the flow by reducing interparticulate friction. Mg stearate is mainly used as lubricant but also can be used as glidant (< 1%).
Notes: <number>

## Slide 26: B. Antiadherents: -Many powders are prone to adhere to the punches ʺsticking" or ʺpickingʺ, which is affected by the moisture content of the powder. - Such adherence specially occurred if the tablet punches have markings or symbols.
Examples of antiadherents:
-Mg stearate
-Talc
-Starch
Notes: <number>

## Slide 27: C. Lubricants: Lubricants are included in all tablet preparations. High friction during tableting can cause serious problems; inadequate tablet quality (tablet fragmentation during ejection) and may even stop production. They improve the rate of flow of the tablet granulation, prevent adhesion of the tablet material to the surface of the dies and punches, reduce interparticle friction, and facilitate the ejection of the tablets from the die cavity. The lubricant should be finely divided by passing through a 100-mesh nylon cloth onto the granulation (bolting the lubricant). Examples for lubricants - Stearic acid and its salts. - Mg stearate is the most commonly used lubricant owing to its superior lubricant property (<1% by weight). - Talc 5% concentration. - Waxes and hydrogenated vegetable oils.
Notes: <number>

## Slide 28: Problems due to lubricants 1- They may reduce tablet strength (HOW?) due to their interference with the bonding between the particles during compression. { bec. they are mainly hydrophobic and lubricating and thus may counteract the role of the binder}. 2- They may retard tablet disintegration and dissolution such as magnesium stearate (WHY?) because most lubricants are hydrophobic (counteract the role of disintegrant). To overcome these waterproofing characteristics, sodium lauryl sulfate is sometimes included. 3- Alkaline metal stearates (aluminum stearate) and talc are incompatible with some drugs e.g. aspirin and ascorbic acid. It is preferable to use hydrogenated vegetable oil or stearic acid with asprin.
Notes: <number>

## Slide 29: How to avoid this negative effect? 1- Minimum amount of lubricant is to be used. 2- More hydrophilic substances are suggested as alternatives e.g. surfactants and polyethylene glycol (PEG). 3- Combination hydrophobic and hydrophilic substances may be also useful. 4- Lubricants are added to granules before compression in a finely divided form.
Notes: <number>

## Slide 30: V- Coloring agents (Colorants): They are added to the tablet formulation to provide product identification and acceptable appearance.
- All colorants used in pharmaceuticals must be approved and certified by the FDA.
- Colorants are often accomplished during coating, but can be also
included in the formulation prior to compaction. In the latter case, the colorant can be added as a soluble dye (wet granulation process) or insoluble lakes (direct compression).
Notes: <number>

## Slide 31: VI- Flavoring agents & sweeteners: - They are usually limited to chewable tablets or tablets that are intended to dissolve in mouth, to impart pleasant taste to mask unpleasant taste. Flavoring agents: - Water-soluble flavours usually have poor stability. For this reason flavour oils or dry powders are typically used. - Oil flavors may be added to tablet granules just before compression (WHY?) because they are sensitive to moisture and volatilization upon heating (during drying process). - Since oils interfere with flowability and compressibility of the granules, minimum amount of the flavouring agent (0.5% of the granulation) is used to avoid their negative effect on the tablet characteristics.
Notes: <number>

## Slide 32: Sweetening agents: - Some sweeteners may come from the diluent (e.g. lactose and mannitol). - Artificial sweeteners such as Saccharine and Aspartame may be also included. - Saccharine has an unpleasant after taste. - Aspartame is unstable in presence of moisture and heat.
Examples of Sweeteners :
Saccharin is about 400 times sweeter than sucrose but it has bitter aftertaste , which can be minimize by the addition of 1% of sod. Chloride .
Aspartame is about 180 times sweetener than sucrose .
Notes: <number>