## Slide 1: Unit 5 COMBINATIONAL CIRCUITS-1
College of Computer and Information Sciences
Department of Computer Science
CSC 220: Computer Organization

## Slide 2
Unit 5: Combinational Circuits-1
Overview
  Introduction to Combinational Circuits
  Adder
  Ripple Carry Adder
  Subtraction
  Adder/Subtractor
Chapter-3
M. Morris Mano, Charles R. Kime and Tom Martin, Logic and Computer Design Fundamentals, Global (5th) Edition, Pearson Education Limited, 2016. ISBN: 9781292096124

## Slide 5: Adder
Design an Adder for 1-bit numbers?
1. Specification: 2 inputs (X,Y) 2 outputs (C,S)

## Slide 6: Adder
Design an Adder for 1-bit numbers?
1. Specification: 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 7: Adder
Design an Adder for 1-bit numbers?
1. Specification: 3. Optimization/Circuit 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 8: Half Adder
This adder is called a Half Adder
Q: Why?
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 9: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit

## Slide 10: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
X
YZ
0
1
00 01 11 10
0 1 0 1
1 0 1 0
X
YZ
0
1
00 01 11 10
0 0 1 0
0 1 1 1
Sum
Carry
S = X’Y’Z + X’YZ’ + XY’Z’ +XYZ
= X  Y  Z
C = XY + YZ + XZ

## Slide 11: Full Adder = 2 Half Adders
Manipulating the Equations:
S = X  Y  Z
C = XY + XZ + YZ

## Slide 12: Full Adder = 2 Half Adders
Manipulating the Equations:
S = ( X  Y )  Z
C = XY + XZ + YZ
= XY + XYZ + XY’Z + X’YZ + XYZ
= XY( 1 + Z) + Z(XY’ + X’Y)
= XY + Z(X  Y )

## Slide 13: Full Adder = 2 Half Adders
Manipulating the Equations:
S = ( X  Y )  Z
C = XY + XZ + YZ = XY + Z(X  Y )
Src: Mano’s Book
Think of Z as a carry in

## Slide 14: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ?
    Outputs ?
    What is the size of the truth table?
    How many functions to optimize?

## Slide 15: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ? 9 inputs
    Outputs ? 5 outputs
    What is the size of the truth table? 512 rows!
    How many functions to optimize? 5 functions

## Slide 16: Ripple Carry Adder
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
Use Z in the circuit as a Cin
1 0 0 0
0 1 0 1
0 1 1 0
1 0 1 1

## Slide 17: Binary Parallel Adder
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
This adder is called ripple carry adder
Src: Mano’s Book

## Slide 18: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?

## Slide 19: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?
1
S = A + ( -B)
Src: Mano’s Book

## Slide 20: Adder/Subtractor
How to build a circuit that performs both addition and subtraction?

## Slide 21: Adder/Subtractor
Src: Mano’s Book
Using full adders and XOR we can build an Adder/Subtractor!
0 : Add
1: subtract

## Slide 22: Binary Parallel Adder (Again)
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
This adder is called ripple carry adder
Src: Mano’s Book

## Slide 23: Carry Look Ahead Adder
How to reduce propagation delay of ripple carry adders?
Carry look ahead adder: All carries are computed as a function of C0 (independent of n !)
It works on the following standard principles:
  A carry bit is generated when both input bits Ai and Bi are 1, or
  When one of input bits is 1, and a carry in bit exists
Cn Cn-1…….Ci……….C2C1C0
An-1…….Ai……….A2A1A0
Bn-1…….Bi……….B2B1B0
Sn Sn-1…….Si……….S2S1S0
Carry Out
Carry bits