## Slide 1: Unit 9 Counters & RAM
College of Computer and Information Sciences
Department of Computer Science
CSC 220: Computer Organization

## Slide 2
Unit 9: Counters and RAM
Overview
  Asynchronous (Ripple) Counters
  A complex Counter
  Introduction to RAM
    Size
    Reading a RAM
    Writing to a RAM
Chapter-6, 7
M. Morris Mano, Charles R. Kime and Tom Martin, Logic and Computer Design Fundamentals, Global (5th) Edition, Pearson Education Limited, 2016. ISBN: 9781292096124

## Slide 3: Asynchronous (Ripple) Counters
Example: 2-bit ripple binary counter.
Output of one flip-flop is connected to the clock input of the next more-significant flip-flop.
Timing diagram
00  01  10  11  00 ...
4
3
2
1
CLK
Q0
Q0
Q1
1
1
1
1
0
0
0
0
0
0

## Slide 4: Asynchronous (Ripple) Counters
Example: 3-bit ripple binary counter.
4
3
2
1
CLK
Q0
Q1
1
1
1
1
0
0
0
0
0
0
8
7
6
5
1
1
0
0
1
1
0
0
Q2
0
0
0
0
1
1
1
1
0
Recycles back to 0

## Slide 5: Asyn. Counters with MOD no. < 2n
Decade counters (or BCD counters) are counters with 10 states (modulus-10) in their sequence. They are commonly used in daily life (e.g.: utility meters, odometers, etc.).
Design an asynchronous decade counter.
D
CLK
HIGH
K
J
C
CLR
Q
K
J
C
CLR
Q
C
K
J
C
CLR
Q
B
K
J
C
CLR
Q
A
(A.C)'

## Slide 6: Asynchronous Down Counters
So far we are dealing with up counters. Down counters, on the other hand, count downward from a maximum value to zero, and repeat.
Example: A 3-bit binary (MOD-23) down counter.
K
J
K
J
Q1
Q0
C
C
K
J
C
Q2 (MSB)
CLK
1
Q
Q'
Q
Q'
Q
Q'
Q
Q'
3-bit binary up counter
3-bit binary down counter
K
J
K
J
Q1
Q0
C
C
K
J
C
Q2 (MSB)
CLK
1
Q
Q'
Q
Q'
Q
Q'
Q
Q'

## Slide 7: Asyn. Counters with MOD no. < 2n
Exercise: How to construct an asynchronous MOD-5 counter? MOD-7 counter? MOD-12 counter?
Question: The following is a MOD-? counter?
K
J
Q
Q
CLR
C
B
A
C
D
E F
All J = K = 1.
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
D
E
F

## Slide 8: Asynchronous (Ripple) Counters
Propagation delays in an asynchronous (ripple-clocked) binary counter.
If the accumulated delay is greater than the clock pulse, some counter states may be misrepresented!
4
3
2
1
CLK
Q0
Q1
Q2
tPLH
(CLK to Q0)
tPHL (CLK to Q0)
tPLH (Q0 to Q1)
tPHL (CLK to Q0)
tPHL (Q0 to Q1)
tPLH (Q1 to Q2)

## Slide 9: 4-bit Ring Counter
So on each successive clock pulse, the counter circulates the same data bit between the four flip-flops over and over again around the “ring” every fourth clock cycle. But in order to cycle the data correctly around the counter we must first “load” the counter with a suitable data pattern as all logic “0’s” or all logic “1’s” outputted at each clock cycle would make the ring counter invalid.
A “CLEAR” signal is firstly applied to all the flip-flops together in order to “RESET” their outputs to a logic “0” level and then a “PRESET” pulse is applied to the input of the first flip-flop ( FFA ) before the clock pulses are applied. This then places a single logic “1” value into the circuit of the ring counter.

## Slide 21: RTL and Memory
While memory transfers are similar to register transfers, we usually identify them differently. Specifically, memory to register transfers are called read operations, while register to memory transfers are called write operations. Both require specification of the memory location to be used (which can be done through a special register or a special bus) and a storage location which will hold the result of a read or which holds the data to be written.

## Slide 22
RTL expressions for a Read operation, assuming the use of an address registers:
RTL expressions for a Write operation, assuming use of a data register:

## Slide 23
Register to Memory Transfers are denoted using square brackets surrounding the memory address.
  e.g. DR  M[AR] (Read operation)
  e.g. M[AR]  DR (Write operation)