## Slide 1: UNIT 2
Darcy Law and Laboratory and Field Methods to determine aquifer properties

## Slide 2: Darcy Law
Henry Philibert Gaspard Darcy was French Engineer born on June 10, 1803 in Dijon, France. In 1856, carried out experiments while researching sand filters that lead to Darcy’s Law.
The law states that the flow rate (Q) through a porous medium is
  directly proportion to the head loss,
  directly proportional to the cross sectional area through which the water is flowing and
  inversely proportional to the length of the flow path.
Darcy Law allows an estimate of the velocity or flow rate moving within the aquifer the average time of travel from the head of the aquifer to a point located downstream .
Darcy’s law provides an accurate description of the flow of ground water in almost all hydrogeologic environments.

## Slide 3: Darcy’s Experiments
Discharge (Q) is
  Proportional to
  Area (A)
  Head difference (dh)
  Inversely proportional to
  Length (dl)
Coefficient of proportionality is
  K = hydraulic conductivity

## Slide 4: Darcy Law
Darcy measurements showed that the flow rate Q is directly proportional to the head loss (dh) and the cross-sectional area (A) of flow.
Q α dh, Q α A
And inversely proportional to the length of the flow path
Q α 1/dl
The above equations can be rearranged as
Q α (dh*A)/dl
Introducing the proportionality constant K in the above equation we get the Darcy Law which can be written as
Q = -K(dh*A)/dl or K*I*A (I = dh/dl)
The constant K is called hydraulic conductivity and depends both on the porous medium and on the fluid passing through it. The negative sign was introduced to obtain a positive value for the discharge; indeed, the groundwater flows in the direction of the decreasing head, which is negative.

## Slide 5: Darcy Law
A horizontal pipe filled with sand is used to demonstrate Darcy’s experiment.
Water is applied under pressure through end A, flows through the pipe, and discharges at end B.
Water pressure is measured using piezometer tubes (thin vertical pipes installed at each end of the horizontal pipe).
The difference in hydraulic head (between points A and B) is dh (change in height).
Dividing this by the flow length (i.e. the distance between the two tubes), dl the hydraulic gradient (I) is obtained.

## Slide 6: Darcy Law
The velocity of groundwater is based on hydraulic conductivity (K), as well as the hydraulic head (I).
The specific discharge or Darcy velocity (v) is obtained by dividing the flow rate (Q) by the cross sectional area.
The Darcy Law can be re-written as
Q/A = K*I where Q/A = vD (Darcy Velocity)

## Slide 7: Darcy Velocity
v is the specific discharge (Darcy velocity).
Specific discharge has units of velocity (L/T).
(–) indicates that v occurs in the direction of the decreasing head.
The specific discharge is a macroscopic concept, and is easily measured.
It should be noted that Darcy’s velocity is different from the microscopic velocities associated with the actual paths of individual particles of water as they wind their way through the grains of sand.
The microscopic velocities are real, but are probably impossible to measure.

## Slide 8: Darcy Velocity and Seepage Velocity
Darcy velocity is a fictitious velocity since it assumes that flow occurs across the entire cross-section of the soil sample.
Flow actually takes place only through interconnected pore channels.
From the Continuity Equation: Q = A*vD = AV *vs
Where : Q = flow rate,
A = total cross-sectional area of material,
AV = area of voids,
vs = seepage velocity and
vD = Darcy velocity

## Slide 9: Darcy Velocity and Seepage Velocity
Linear flow paths assumed in Darcy’s law
True flow paths

## Slide 10: Darcy Velocity and Seepage Velocity
Therefore: vS = vD ( A/AV)
Multiplying both sides by the length of the medium (L)
vS = vD ( AL / AVL ) = vD ( VT / VV )
Where: VT = total volume VV = void volume
By Definition, Vv / VT = n, the soil porosity thus
vS = vD / n
Seepage Velocity = Darcy Velocity x Rock/Soil Porosity

## Slide 11: Darcy Law Example
A confined aquifer has a source of recharge. K for the aquifer is 50 m/day.
The water level in two wells 1000 m apart is 55 m and 50 m respectively.
The average thickness of the aquifer is 30 m, and the average width of aquifer is 5 km.
Calculate the flow rate and the seepage velocity if the effective porosity is 0.27.

## Slide 12: Validity of Darcy’s Law
In applying Darcy’s law it is important to know the range of validity within which it is applicable.
For flow in pipes or other large sections, the Reynolds number which expresses the dimensionless ratio of inertial to viscous forces, serves as a criterion to distinguish between laminar and turbulent flow.
Reynolds number (NR) is expresses as
NR = ρvD/μ
Where ρ is the fluid density, v is the velocity, D is the diameter of the pipe and μ is the viscosity of the fluid.
Experiments show that Darcy’s law is valid for NR < 1 and does not depart seriously up to NR = 1
LAMINAR FLOW
TURBULENT FLOW

## Slide 13: Validity of Darcy’s Law
Fortunately, most natural underground flow occurs with NR < 1 , so Darcy’s Law is applicable.
Deviation from Darcy’s law can occur when steep hydraulic gradients exist, such as near pumped wells.
Turbulent flow can also be found in rocks such as basalt or limestone that contain large underground openings.
Turbulent Flow and Laminar Flow

## Slide 14: Condition of Darcy Law
Darcy’s Law holds for:
  Saturated flow and unsaturated flow
  Steady-state and transient flow
  Flow in aquifers and aquitards
  Flow in homogeneous and heterogeneous systems
  Flow in isotropic or anisotropic media
  Flow in rocks and granular media

## Slide 15: Permeabilty
The permeability of a rock or soil defines its ability to transmit a fluid.
Intrinsic Permeability
It is the portion of hydraulic conductivity which is representative of the properties of the porous medium alone (not the fluid)
It is a function of size of the openings through which the fluid moves
k = C d2
Where C = dimensionless constant,
d = mean pore diameter
Dimensions of Intrinsic permeability is L2 which is the same as Area.
Intrinsic permeability thus depends only on the property of the medium and not the fluid.

## Slide 16: Permeability
Hydraulic Conductivity
On the other hand Hydraulic Conductivity K depends on the porous medium property as well as the property of the fluid passing through the medium and is expressed
K = kρg/μ
Where k is Intrinsic permeability, Porous Medium Property
μ is dynamic viscosity,
ρ is fluid density and Fluid Property
g is acceleration due to gravity.
Hydraulic conductivity (K) defines the rate of movement of water through a porous medium such as a soil or aquifer.
Hydraulic conductivity (K) is defined as the flow volume per unit cross-sectional area an aquifer per unit change in the hydraulic gradient.
This translates to SI units of m3/m2/day or m/d, but other measurement units are commonly used and has the same units as velocity

## Slide 17: Permeability
For practical work in groundwater hydrology, where water is the prevailing fluid, hydraulic conductivity K is used.
A medium has a unit hydraulic conductivity if it will transmit in a unit time a unit volume of groundwater at the prevailing kinematic viscosity through a section of unit area, measured at right angles to the direction of flow under a unit hydraulic gradient.
The units of K is L/T (m/day or m/min or m/sec)
Kinematic viscosity is equal to dynamic viscosity divided by fluid density

## Slide 18: Permeability
The term transmissivity T is widely used in hydrogeology.
It is defined as the flow volume per unit cross-sectional area an aquifer of unit saturated thickness per unit change in the hydraulic gradient.
T = Kb
where K is the Hydraulic conductivity and b is the saturated thickness of the aquifer.
The units of K is L2/T (m2/day or m2/min or m2/sec)
where b is the saturated thickness of the aquifer.

## Slide 19: Hydraulic Conductivity of Geologic Materials
The hydraulic conductivity of soil or rock depends on a variety of physical factors including
Porosity
Particle size and distribution
Shape of particles
Arrangement of particles
In general for unconsolidated porous media, hydraulic conductivity varies with particle size; clayey material exhibit low values of hydraulic conductivity, whereas sands and gravels display high values.

## Slide 20: Permeability

## Slide 21: Laboratory measurements for Hydraulic Conductivity
In the laboratory, hydraulic conductivity can be determined by a permeameter, in which flow is maintained through a small sample of material while measurements of flow rate and head loss are made.
The constant head permeameter shown here can measure the hydraulic conductivities of consolidated or unconsolidated formations under low heads.
Water enters the medium cylinder through the bottom and is collected as overflow after passing through the material.
h

## Slide 22: Laboratory measurements for Hydraulic Conductivity
From Darcy’s law it follows that the hydraulic conductivity can be obtained from
Where V is the flow volume in time t and the other dimensions A, L and h are shown in the figure.
It is important to fully saturate the sample to remove entrapped air.
Several measurements at different heads in a series gives a reliable result of the K measurement.
h

## Slide 23: Laboratory measurements for Hydraulic Conductivity
To calculate hydraulic conductivity in falling-head method, a mass balance approach is taken.
Note that the rate of water discharges from the tube into the permeameter is equal to the product of the area of the tube and the rate of fluid movement through the tube:
where dh/dt is the rate of fluid movement through the tube, which is also the rate of change in the hydraulic head driving the flow into the permeameter.

## Slide 24: Laboratory measurements for Hydraulic Conductivity
On the other hand, the rate at which water discharges from the permeameter is given by:
where h refers to the difference in hydraulic head at the inlet and the outlet, and L is the length of the sample Notice that h decreases with time, hence the flow also decreases with time.
At any one instant, the flow entering the permeameter must equal the flow leaving the permeameter, hence:

## Slide 25: Laboratory measurements for Hydraulic Conductivity
Rearranging
Integrating from time zero to time t, during which the head decreases from ho to h
Since the cross-sectional areas are proportional to the square of the diameters of the falling head tube, dtube, and the permeameter, dperm, the above equation can be further simplified to:

## Slide 26: Laboratory measurements for Hydraulic Conductivity
where K is the hydraulic conductivity
L is the sample length,
ho is the initial head in the falling tube,
h is the final head in the falling tube,
t the time that it takes for the head to drop from ho to h,
dtube is the diameter of the falling tube, and
dperm is the inside diameter of the permeameter.

## Slide 27: Laboratory measurements for Hydraulic Conductivity
Permeameter results may bear little relation to actual field hydraulic conductivity because
Undisturbed samples of unconsolidated material are difficult to obtain, (Disturbed sample experience changes in porosity, packing and grain orientation which modifies the hydraulic conductivity).
One or even several samples may not represent the hydraulic conductivity of the entire aquifer, (Actual aquifer hydraulic conductivity may vary with depths and location).
Directional properties of hydraulic conductivity may not be identified with laboratory methods.

## Slide 28: Laboratory measurements for Hydraulic Conductivity
Tracer Tests
Field determinations of hydraulic conductivity can be made by measuring the time interval for a water tracer between two observation wells or test holes.
For the tracer, a dye, such as sodium fluorescein, or a salt such as calcium chloride, is convenient, inexpensive, easy to detect and safe.

## Slide 29: Laboratory measurements for Hydraulic Conductivity
The figure shows the cross-section of a portion of an unconfined aquifer with groundwater flowing from hole A towards hole B.
The tracer is injected in hole A and the samples of water are taken from hole B to determine the travel time for tracer.
Where K is the hydraulic conductivity,α is the porosity and h and L are shown in the figure

## Slide 30: Laboratory measurements for Hydraulic Conductivity
Va can also be expressed as distance over time or L/t. Equating these in the previous equation and solving for K yields.
Though this procedure is simple but the results are only the approximation of K because of serious limitations in the field.

## Slide 31: Laboratory measurements for Hydraulic Conductivity
Limitations of tracer tests are the following:
The holes need to be close together, otherwise the travel time interval can be excessively long.
Unless the flow direction is accurately known, the tracer may miss the downstream hole entirely.
If the aquifer is layered with different hydraulic conductivities, the first arrival of the tracer will result in a conductivity considerably larger than the average of the aquifer.

## Slide 32: Laboratory measurements for Hydraulic Conductivity
A tracer test is conducted to determine the hydraulic conductivity of an unconfined aquifer. The water levels in the two observation wells 20 m apart are 18.4 m and 17.1 m respectively. The tracer injected in the first well reaches the second well in 167 hours. Calculate the hydraulic conductivity of the unconfined aquifer if the porosity of the formation is 0.25.

## Slide 33: Laboratory measurements for Hydraulic Conductivity
The most reliable method for estimating aquifer hydraulic conductivity is by pumping test of wells.
Based on observation of water levels near pumping wells, an integrated K value over a big section of the aquifer can be obtained
The reliability of this method is much superior to the methods discussed earlier.

## Slide 34: Hydraulic Conductivity for Anisotropic Aquifer
All the pervious calculations of hydraulic conductivity was based on the assumption that the geologic material was homogeneous and isotropic, implying that the hydraulic conductivity was equal in all directions.
However, for undisturbed , unconsolidated alluvial material it is rarely the case.

## Slide 35
Consider an aquifer consisting of two horizontal layers, each individually isotropic with different thickness and conductivities as shown in the figure.
For horizontal flow parallel to the layers, the flow in the upper layer per unit width is
q1 = K1iz1
Where i is the hydraulic gradient and K1 and z1 are shown in the figure.
Because i must be the same in each layer for horizontal flow it follows that the total horizontal flow qx is
qx = q1 + q2 = i(K1z1 + K2z2)
z1
z2
K1
K2
q1
q2
qz
Hydraulic Conductivity for Anisotropic Aquifer(Kx)

## Slide 36: Hydraulic Conductivity for Anisotropic Aquifer(Kx)
For a homogeneous system it will be expressed as
qx = Kxi(z1 + z2)
Where Kx is the horizontal hydraulic conductivity for the entire system.
Therefore the equivalent horizontal hydraulic conductivity of a stratified aquifer can be defined as
Kxi(z1 + z2) = i(K1z1 + K2z2) or
Kx = K1z1 + K2z2
z1 + z2

## Slide 37: Hydraulic Conductivity for Anisotropic Aquifer(Kz)
Now for the vertical flow through the two layers in the figure
Where dh1 is the head loss within the first layer. Solving for the head loss we get
From continuity equation, qz must be the same for the other layers so that the total head loss is

## Slide 38: Hydraulic Conductivity for Anisotropic Aquifer(Kz)
For a homogeneous system
Where Kz is the vertical hydraulic conductivity for the entire system. Rearranging yields we get
Therefore equating with the equation for heterogeneous aquifer we get
This defines the vertical hydraulic conductivity for a stratified aquifer

## Slide 39: Hydraulic Conductivity for Anisotropic Aquifer
The horizontal hydraulic conductivity in alluvium is normally greater than the vertical direction
For a two layered case it follows that

## Slide 40: Example

## Slide 41: Example

## Slide 42: Exercise
Calculate the equivalent horizontal and vertical hydraulic conductivities for the figure given below.

## Slide 43: Flow Net
A flow net is a graphical representation of a flow pattern. It consists of families of flow lines and Equipotential lines.
A Flow line or stream line is the mean path of flow of a particle of water. Equipotential lines represent contours of equal head.
When constructing a flow net the flow lines are drawn orthogonal (right angles) to the Equipotential lines, resulting in a pattern of squares (or rectangles), with the ratio of the mean dimensions of each pattern equal.
To construct a flow net for a region, it is necessary to have sufficient groundwater elevation and aquifer test data.

## Slide 44: Assumptions of Flow net Analysis
The aquifer is homogeneous, isotropic and is fully saturated.
The flow field is at steady-state.
The aquifer material and water are incompressible.
Flow is laminar and Darcy’s law is applicable.
Boundary conditions are known.
Stream lines and Equipotential lines intersect at right angles.
Flow quantity between all parts of adjacent streamlines is same.
Energy loss between all pairs of Equipotential lines is same.

## Slide 45: Flow net analysis
Consider a portion of a flow net. The hydraulic gradient , (Equation 1)
and the constant flow between two adjacent flow lines, (Equation 2)
For unit thickness and for the square of the flow net, the approximation ds ≈ dm
So, Eq. 2 reduces to

## Slide 46: Flow net analysis
Applying to entire flow net, when total head is divided into n squares between any two adjacent flow lines,
If the flow is divided into m channels by flow lines, then the total flow,
So, the geometry of the flow net together with the hydraulic conductivity and head loss enable the total flow to be computed directly.

## Slide 47: Flow net analysis
When a contour map of groundwater levels contains closed contours around a group of wells of known total discharge (Q), then the aquifer transmissivity (T) can be calculated.
For an area of uniform groundwater flow, the areas with wide contour spacing (flat gradient) possess higher hydraulic conductivity (k) than those of narrow spacing.
Therefore, prospects for a production well are better near flat gradient.

## Slide 48: Advantages of Flow net
Direct calculation of total flow (Q)
Determination of aquifer transmissivity (T)
Direction of flow
Location of new water wells.

## Slide 49: Groundwater flow direction
Draw a line connecting the points of maximum and minimum water level. In the above figure it will be between Point A and Point C.
Find the difference between the maximum and minimum water level. In Figure 1 above C = 14m (maximum) and A = 10m (minimum). Difference in water level = 14m - 10m = 4m
Divide the line connecting the points of maximum and minimum water level into as many parts as the difference between the two. In the above case it will be 4, (see Figure 2)
Join the point of 12m on the line AC with B. This line represents the water level contour for 12m.
Draw lines parallel to the 12m contour at every 1m interval. This will represent the contours of 10 m, 11m, 12m, 13m and 14m respectively. See the blue lines in Figure 2.
The groundwater will flow from the higher elevation to the lower elevation perpendicular to the water level contours. The red arrow in Figure 2 shows the groundwater flow direction
Figure 1
Figure 2