## Slide 1: Vital signs

## Slide 2: Outline
Vital Signs Definition
Temperature
Pulse Rate
Respiratory Rate
Blood Pressure
Pain

## Slide 3: Vital sign
physical signs that provide data to determine a person’s state of health
indicate an individual is alive, such as temperature, pulse rate, respiratory rate (TPR), and blood pressure (BP).

## Slide 4: Measuring Body Temperature
Purposes
To establish baseline data for subsequent evaluation .
To identify whether the core body temperature is within normal range or not (e.g. infection) and response to treatment.

## Slide 5: Types of Thermometers
Electronic thermometers
most accurate if placed in sublingual pocket.

## Slide 6: Types of Thermometers
Tympanic membrane thermometer
measures the temperature inside of the ear.
Especially appropriate for infants and young children

## Slide 7: Types of Thermometers
Glass and mercury thermometers
a glass tube with mercury inside of the tube.

## Slide 8: Sites for taking the Temperature
SITE | ADVANTAGES | DISADVANTAGES
ORAL | Accessible and convenient | Thermometers can be broken
 |  | Inaccurate if client has just ingested hot or cold fluid, or smoked
RECTAL | Reliable measurement (lateral or sim’s position) | Inconvenient and more unpleasant; difficult for client who cannot turn to side
 |  | Could injure the rectum following surgery
 |  | Presence of stool may interfere with thermometer placement
AXILLARY | Safe and noninvasive | Thermometer must be left in place for a long time
TYMPANIC MEMBRANES | Readily accessible; reflects the core temperature, very fast | Can be uncomfortable and involves risk of injuring the membrane if inserted too far
 |  | Presence of cerumen can affect the reading
TEMPORAL ARTERY | Safe and non invasive , very fast | Requires electronic equipment (expensive / unavailable) ;
 |  | Variation in technique if the client has perspiration on the forehead

## Slide 9: Sites for taking theTemperature

## Slide 10: Assessment of peripheral Pulse
Purpose :
  To identify baseline and whether the pulse rate is within normal range and the pulse rhythm is regular and the pulse volume is appropriate .

## Slide 11: Pulse sites

## Slide 13: Implementation :
6- Palpate and count the pulse . Place 3 or 2 middle fingers lightly and squarely over the pulse point .
7- Count for 15 seconds and multiply by 4 .
8- Record the pulse on the worksheet .
9- Assess the pulse rhythm and strength .
10- Document the pulse rate on the patient’s record .
11- Hand wash

## Slide 14: C-Assessment of Respiration :
Purposes :
To acquire baseline data and monitor abnormal respiration and respiratory patterns against which future measurements can be compared.

## Slide 15: Planning
Implementation :
Preparation:
For a routine assessment of respiration , determine the client’s activity schedule and choose a suitable time to monitor the respirations . A client who has been exercising will need to rest for a few minutes to permit the accelerated respiratory rate to return to normal .

## Slide 16: considering
never to notify the patient that you will assess respiration.
count the respiratory rate .
5Observe the respiration for depth regularity .

## Slide 17: Assessment of Blood Pressure
Purpose :
1-To obtain a baseline measure of arterial blood pressure and monitor changes in blood pressure for subsequent evaluation .

## Slide 18: Equipment
Sphygmomanometer
  Aneroid
  Mercurial
  Stethoscope

## Slide 19: Sphygmomanometer
Pediatric
Adult

## Slide 20: Parts of a stethoscope
Diaphragm= circular, flat surface- transmits high pitched sounds ( Bowel, lung, heart sounds
Bell= bowl shaped- transmits low pitched sounds (heart and vascular sounds)

## Slide 21
Preparation :
2- Make sure that the client has not smoked within 30 minutes

## Slide 23
THANK TOU