## Slide 1: PETROLOGY
Is a branch of geology, which deals with study of rocks (Petro=rock, Logos=study)
ROCKS
IGNEOUS
-most abundant
-primary rocks
-source is magma or lava
SEDIMENTARY
-thin veener above the Sial and Sima in Oceanic and Continental Crusts
-secondary rocks
METAMORPHIC
-proportion is similar to that of Igneous rocks
-change of forms of Ig. And Sed. Due to Temprature, Pressure and Chemical Fluids

## Slide 2: Importance of petrology in civil Engg.
It provides an opportunity to interpret the physical properties of individual rocks, likewise: texture, structure, mineral composition, chemical composition etc.
This helps in knowing the strength, durability, colour, appearance, workability etc.
These properties are very important for CE to know because different rocks are suitable for different purposes and no rock is ideal or best suited for all purpose.

## Slide 3
Granite: hard, competent, durable => suitable for foundation
Limestone: comparatively soft=> best for flooring
Marble: soft and attractive=> flooring/sculpturing etc.
Sandstone: sculpturing, wall etc.

## Slide 4
IGNEOUS ROCKS: The rocks formed through volcanic action OR
The rocks which are derived from a molten mass “magma or lava”
SOURCE OF IGNEOUS ROCKS:
Magma: Molten mass comprising most abundant elements in
earth – Si, Al, Fe, Ca, Mg, K, H & O. Where the SiO2
is most abundant amongst all.
Temperature of Magma- 10400 to 12000 C
VOLCANO: A gap in the Earth’s Crust where molten rocks and other material escape onto the Earth’s surface

## Slide 5: Influencing Factors for Magma Flow and Formation of Igneous Rocks
Overlying sedimentary rocks as overburden plays important role in formation of igneous bodies eg: dykes, sills, laccoliths, bysmaliths, phacoliths, lopolith, volcanic necks, batholiths and chonoliths.
The beddings in the sedimentary rocks facilitates the magma to move through or intrude/inject through the weak planes

## Slide 6
KINDS OF IGNEOUS ROCK

## Slide 7
FLUIDITY OF MAGMA
Fluidity or Viscosity of magma depends on content (%) of Silica
Silica Rich
known as Acidic magma
More viscous, so do not spreads and piles up at one place
Silica poor
-Known as Basic magma
-Less viscous, moves faster and occupies larger area
However, the viscosity of magma is considerably influenced by
temperature too. When temperature is less-more viscous and when
High temperature- less viscous.

## Slide 8
BROAD CLASSIFICATION OF IGNEOUS ROCKS
Volcanic rocks
(Extrusive rocks)
-Lava or Magma flows
-Pyroclastic flows
Intermediate rocks
(Hypabyssal rocks)
Plutonic rocks
(Intrusive rocks)
-dykes, sills, batholiths, laccoliths etc.
Name comes from Greek god of the underworld - Pluto

## Slide 9
FORMS OF VOLCANIC ROCKS
Extrusive (volcanic) igneous rocks form when molten rock erupts from Earth's interior through a volcano or fissure and cools rapidly at the surface in form of Lava and hence it does not have any specific shape
Lava flows: On eruption lava simply flows on the surface and on the basis of surface appearance, lava flows are described as blocky lava and ropy lava

## Slide 10
Block Lava: is less mobile
i.e. more viscous and has a
Rough and irregular surface. Vesicles are few and irregular in shape
When cools down it result into angular, chunky texture. This causes the lava to thicken and to break apart as the flow continues to move down slope. Such a texture is referred to as a-a, probably because of the pain inflicted on a person trying to walk across such a flow.

## Slide 11
Ropy Lava: is more mobile i.e. less viscous, it has a wrinkled but smooth and shiny surface on cooling.
Vesicles are more in number, small-spherical in shape.

## Slide 12
PYROCLASTS OR PYROCLASTIC:
Extrusive igneous rock texture referred to as pyroclastic. This texture results from a very explosive eruption, which sends not only lava flying through the air, but also fragments of the volcano itself. All airborne volcanic fragments, referred to as pyroclasts

## Slide 13
The rock fragments thrown out during volcanic eruption are called
Pyroclasts.
Pyroclasts come in many sizes: the smallest are called ash, slightly larger are lapilli, and the biggest are called blocks or bombs.
Based of shape and size they are categorized
ash
lapilli

## Slide 14
A large pyroclasts are known as volcanic bombs. Typical shape with head and a tail. Bombs can result into severe damage if they strike.