## Slide 1: Water pollution

## Slide 3: Unpolluted water is essential for :
• A safe drinking water supply.
• Maintaining fish habitats
• Supporting water sports e.g. boating, swimming, water skiing
• Water for crops and livestock
• Industrial use

## Slide 4: Water Pollution
Any chemical, biological and physical change in water quality that has a harmful effect on living organisms or makes it unusable for agriculture

## Slide 5: Types of Pollutants
Disease-causing Agents (biological)i.e pathogens
organic waste
Water-soluble Inorganic Chemicals – acids, toxic metals
Heat – electric and nuclear power plants
Organic Chemicals – oil, pesticides, detergents
Sediment or Suspended Material – erosion, soil
Water-soluble Radioactive Isotopes – radon uranium

## Slide 6: Volume and significance of pollutant
Not all types of pollution act in the same way. Small amounts/ concentrations of some substances e.g. ammonia, metals, pesticides and oil can have very serious impacts.
For example, one litre of oil will be visible and will pollute an area of water equivalent to the size of three football pitches.

## Slide 7: Biological pollution
Escherichia coli
Vibrio sp

## Slide 11: Organic waste
Oxygen is removed from water when organic matter is consumed by bacteria.
Low oxygen conditions may kill fish and other organisms.
Sources of organic matter
Natural inputs-- leaf fall, and vegetation aligning waterways.
Human inputs-- food processing industries, runoff from agricultural areas, and sewage.

## Slide 12
Sewage consists of human wastes and garbage. It also includes water used for laundering or bathing.
Most sewage is treated at a treatment plant that removes the solids and dissolved substances. However, when a treatment plant gets overloaded or has a malfunction, sewage gets dumped into rivers.

## Slide 13
Sewage depletes the dissolved oxygen in water.
Sewage wastes contain nutrients that serve as fertilizers. They cause algae (tiny plants) to bloom in great quantities. When these organisms die, oxygen is used for the process of decomposition, and the fish go without adequate oxygen and sometimes die.
Raw sewage can also cause serious diseases in humans who use the water or eat shellfish from polluted areas.
Sewage may also make waters unhealthy to swim in.

## Slide 14
Fig. 11-23, p. 247
Decomposition Zone
Biological
oxygen demand
Trash fish (carp, gar,
leeches)
Fish absent, fungi, sludge
worms,
bacteria (anaerobic)
Trash fish (carp, gar,
leeches)
8 ppm
8 ppm
Clean Zone
Clean Zone
Recovery Zone
Septic Zone
Types of organisms
Dissolved oxygen (ppm)
Normal clean water organisms(Trout, perch, bass,mayfly, stonefly)
Normal clean water organisms
(Trout, perch, bass,
mayfly, stonefly)
Notes: Figure 11.23: Dilution and decay of degradable, oxygen-demanding wastes and heat in a stream, showing the oxygen sag curve (blue) and the curve of oxygen demand (red). Depending on flow rates and the amount of pollutants, streams recover from pollution by oxygen-demanding wastes and heat if they are given enough time and are not overloaded (Concept 11-5A).
Question: What would be the effect of putting another waste discharge pipe to the right of the one in this picture?
See an animation based on this figure at ThomsonNOW.

## Slide 15: Water-soluble Inorganic Chemicals (Heavy metals)
Most are extremely toxic
  Water soluble
  Readily absorbed into plant or animal tissue
Examples:
  Pesticides
  Arsenic, lead, mercury, other metals

## Slide 16
Sources of Heavy Metals: Industrial
Mercury poisoning—Can cause mental retardation, cerebral palsy, kidney disorders, and damages the nervous system.
Lead poisoning— Causes miscarriages, hearing loss, learning disabilities.
Heavy Metals by Dr. Jena Hamra

## Slide 17
Acid Rain: is a result of industries and cars burning oil and coal and sending sulfur dioxide and nitrogen oxides high into the atmosphere. While in the air they mix with water vapor and turn into sulfuric and nitric acids. Eventually, this harmful acid returns to earth in rain, hail, fog, or snow.

## Slide 18
This acid damages plant life and may eventually kill insects, frogs, and fish in our waters
Acid rain is a worldwide problem because it can be carried in the atmosphere for great distances before falling back to earth.

## Slide 19
Heat:
Thermal Pollution occurs when water is withdrawn, used for cooling purposes (e.g. electric and nuclear power plants), and then heated water is returned to its original source
An increase in temperature, even a few degrees, may significantly alter some aquatic ecosystems

## Slide 20: Organic Chemicals
Oil spills
Oil spills can be caused by:
  Tanker accidents
  Intentional dumping
  pumping operations

## Slide 21
Volatile Organics Compounds immediately kill many of the aquatic organisms and contaminate fish
Heavy oil sinks to ocean bottom where it contaminates crabs, oysters, mussels, clams, etc.
Effects of Oil Spills
© Brooks/Cole Publishing Company / ITP Water Resources and Water Pollution by Paul Rich

## Slide 22
Floating oil coats birds and ocean mammal; and render their insulating fur or feathers useless

## Slide 23: Sediment
Erosion of soil from mining, and farming puts sediment into waterways.
There it alters conditions and can kill organisms.

## Slide 24: Radioactive Wastes
Radioactive wastes can also be a sources of water pollution.
Radioactive wastes stored in underground containers may leak and pollute groundwater. Pollution of the oceans occurs if these wastes are dumped in the ocean.

## Slide 25: Swimming-associated illnesses:
Viruses are believed to be the major cause of swimming-associated illnesses, & are responsible for
gastroenteritis,
hepatitis,
respiratory illness, &
ear, nose, & throat problems.
Other microbial diseases that can be contracted by swimmers include salmonellosis, shigellosis, giardiasis, amoebic dysentery, skin rashes, “pink eye,” & infection caused by E. coli.
The most common symptoms are nausea, diarrhea, vomiting, itching, skin rashes & fever.