## Slide 1
Time Response, Stability, and
Steady State Error

## Slide 2
1 Time Response
Performance of controlled systems can be tested and compared by their responses to certain test signals (Step functions, impulse functions, ramp functions, sinusoidal functions, etc.).
A response of a dynamic system can be analyzed in two parts:
  Steady-state response: The behavior of the output as
  Transient response: The behavior of the output as it goes from an initial state to a final state.
This chapter is devoted to the analysis of system transient response.
The mathematical representation of a system (Transfer function or State space) is used to analyze its transient and steady-state responses to see if these characteristics yield the desired behavior.

## Slide 3
Poles, Zeros, and System Response
Time Response
The output response of a system is the sum of two responses:
1. the forced response (steady-state response or particular solution),
2. the natural response (the homogeneous solution).
Output response = forced response (e.g. constant) + natural response (e.g. exponential)
Poles of a Transfer Function (TF): The values of s that cause
roots of the denominator (characteristic polynomial) of the transfer function
Zeros of a TF: the values of s that cause TF = 0.
roots of the numerator of the transfer function
Example: Poles and Zeros of a First-Order System
Inverse Laplace transform:
System showing input and output
pole-zero plot of the system
where
and
System Output (unit step response)
System Output in time domain (time response)

## Slide 4
Example: Poles and Zeros of First Order System
Evolution of a system response.
Input poles
generates
Forced response
( pole at the origin generated a step function at the output)
Input function
System poles
generates
Natural response
Transfer function
System poles
And zeros
generates
Amplitudes for both the forced and natural responses
(A pole on the real axis generates an exponential response of the form that will decay to zero).

## Slide 5
Evaluating Response using Poles
Problem:
Given the following system, write the output, c(t), in general terms. Specify the forced and natural parts of the solution.
Solution:
Taking inverse Laplace transform,
Each system pole generates an exponential as part of the natural response.
The input's pole generates the forced response.
Forced
response
Natural
response
Poles of the system produce the
Natural response that Will decay to zero

## Slide 6
First-Order System: Time Constant
A first-order system without zero:
If the input is a unit step: then the Laplace
transform of the step response is :
Taking the inverse transform
When
Hence,
the input pole at the origin generated the forced response
The system pole at –a generated the natural response
Significance of parameter a (system pole) (only parameter needed to describe the transient response),

## Slide 7
Some Terminology
(three transient response performance specifications).
1. Time constant : Time it takes for the step response to rise to 63% of its final value.
we can call the parameter (system pole) the exponential frequency (The reciprocal of the time constant)
is related to the speed at which the system responds to a step input.
2. Rise Time : Rise time is defined as the time for the response to go from 0.1 to 0.9 of its final value.
Rise time:
found by solving for the difference in time at c() = 0.9 and c() = 0.1
3. Settling time : The time for the response to reach, and stay within, 2% of its final value.
Lettingand solving for time, , we find the settling time to be

## Slide 8
First-Order Transfer Function via Testing
With a step input, we can measure the time constant and the steady-state value, from which the transfer function can be calculated.
A simple first order system has :
and step response is:
From the response, we identify K and a to obtain the transfer function.
To find a:
To find K: From , the forced response reaches a steady-state value of
Transfer function,
In the time domain (ILT):
and

## Slide 9
General case of second order system
Canonical form
(two finite poles and no zeros)
Second-Order System1
Parameters of First-order system determine the speed of the system.
Parameters of Second-order system determine the form (shape) of the system.
: (Natural Frequency ) the frequency of oscillation of the system without damping.
(D) dimensionless measure describing how oscillations in a system decay.
exponential decay , real part of the pole
For un-damped(without damping) system, , and the poles are on at ,
Hence
For an under-damped system, poles have real part (exponential decay ),
Consider the general system,
System poles
un-damped system
D
Natural Frequency
Exponential decay frequency
Natural frequency
Poles

## Slide 10
Second-Order System2
the general case
(two finite poles and no zeros)
Case1: Overdamped system: () Two real poles
The sign of the discriminant of the denominator polynomial depends on the damping ratio , three cases.
Overdamped system
System poles

## Slide 11
Second-Order System
Case 2: Under-damped Response () : (Two complex poles that come from the system).
Poles from the system:
Where,
Second-order
step response
components
generated by
complex poles
exponential decay
frequency of the
sinusoidal oscillation.
From,

## Slide 12
Case 3: Un-damped Response (: pole at the origin that comes from the input and two imaginary poles that come from the system.
Second-Order System
There is no exponential term, so no decay.
Case 4: Critically Damped Response ( : pole at the origin that comes from the input and two multiple real poles that come from the system.
3
There is no sinusoidal term, so no oscillation.

## Slide 13
Two
Two real poles at
Over-damped responses
Two
Under-damped responses
Two complex poles at
Two
Un-damped responses
Two imaginary poles at
Two
Critically damped responses
Two real poles at
Step responses for second-order system damping cases
Second-Order System
All Together

## Slide 14
Second-Order System As a Function of Damping Ratio
Relationship between the quantities and the pole location.
Solving for the poles of the transfer function
Second-order response as a function of damping ratio
Example
For the system find the value of and report the kind of response expected.
We have
and
System is over-damped.

## Slide 15
Underdamped Second-Order Systems
The nature of the response obtained is related to the value of the damping ratio (over-damped, critically damped, underdamped, and un-damped responses.).
Step response for the general second-order system,
Expanding by partial fractions, (< 1 the underdamped case )
inverse Laplace transform
Where,
The lower the value of ζ, the more oscillatory the response is.
Second-order underdamped responses for damping ratio values

## Slide 16
Underdamped Second-Order Systems
Specifications
Other parameters associated with the underdamped response are rise time, peak time, percent overshoot, and settling time.
Rise time
Peak time
The time required for the waveform to go from 0.1 of the final value to 0.9 of the final value.
The time required to reach the first, or maximum, peak.
percent
overshoot
The amount that the waveform overshoots the steady-state, or final, value at the peak time, expressed as a percentage of the steady-state value.
and
settling time
The time required for the transient's damped oscillations to reach and stay within ±2% of the steady-state value.
Derivation: self study.
Second-order underdamped response specifications

## Slide 17
Under-damped Second-Order Systems
Specifications (continued)
from the Pythagorean theorem
Natural frequency
damped frequency of oscillation,
exponential damping frequency.
inversely proportional to the imaginary part of the pole.
inversely proportional to the real part of the pole.
Damped frequency of oscillation
Damping Ratio

## Slide 18
Under-damped Second-Order Systems
Step Response as Pole moves
poles move in a horizontal direction
(with constant imaginary part )
frequency increases
envelope remains the same (constant real part )
settling time is virtually the same
overshoot increases, the rise time decreases
poles move in a vertical direction
(with constant real part )
poles move in along a constant radial line direction
As the poles move to the left, response damps out more rapidly.
peak time is the same for all waveforms (constant imaginary part )
The percent overshoot remains the same.
The farther the poles are from the origin, the more rapid the response.

## Slide 19
Finding TP, %OS, and TS From Pole Location
Problem:
Solution:
Given the pole plot find , , , %OS, and .
Damping ration,
Natural frequency,
Peak time,
Percent overshoot,
The approximate settling time,

## Slide 20
System Response with Additional Poles
If a system has more than two poles or has zeros, we cannot use the formulas to calculate the performance specifications that we derived.
We need to approximate that system to a second-order system that has just two dominant complex poles.
Assuming two complex poles at
And the real pole at
Time domain step response,

## Slide 21
Comparing Responses of Three-Pole Systems
if the real pole is five times farther to the left than the dominant poles
system is represented by its dominant second-order pair of poles.

## Slide 22
Evaluating Pole-Zero Cancellation
Problem: For any function for which pole-zero cancellation is valid, find the approximate response.
Solution:
The partial-fraction expansion of is
That residue (1) is not negligible. So a 2nd-order step response approximation cannot be made for .
The partial-fraction expansion of is
That residue (0.033) is negligible, so cancel zero and that pole.
Hence, the approximate response,
Effect of a zero on the system: A system with a zero consists of the derivative of the original response and the scaled version of the original response. If the zero is very large, the Laplace transform of the response is approximately the scaled version of the original response. As the zero becomes smaller, the derivative term contributes more to the response and has a greater effect.
Effect of adding a zero to a two-pole system
derivative response
scaled response
pole-zero cancellation

## Slide 23
2. Stability
Stable system: If natural response approaches zero as time approaches infinity (LTI System).
Marginally stable system: If natural response neither decays nor grows but remains constant or oscillates as time approaches infinity.
BIBO (Bounded Input, Bounded Output) yields stable system.
Stable systems have closed-loop transfer functions with poles only in the left-half plane.
Stability is the most important system specification.
the total response of a system

## Slide 24
Routh-Hurwitz Criterion
This method Provides stability information with solving for system poles.
How many poles are in left / right plane or in jw axis, not where
Routh Table Generation:
Denominator:
Completed Routh table

## Slide 25
Routh-Hurwitz Criterion: Example
How many sign changes in the first column  the number of poles in the right-half plane
Two such poles : unstable system.
Any row can be multiplied by a positive number. the row was multiplied by 1/10
Interpreting the Basic Routh Table
the first column
Make the Routh table for the system shown in Figure
PROBLEM:
SOLUTION:
The first step is to find the equivalent closed-loop system
the number of roots of the polynomial that are in the right half-plane is equal to the number of sign changes in the first column.

## Slide 26
Routh-Hurwitz Criterion: Special Cases
1. Zero Only in the First Column
If the first element of a row is zero, division by zero in the next row
Example:

## Slide 27
Routh-Hurwitz Criterion: Special Cases
Zero Only in the First Column: reverse coefficients
Reverse coefficients:
Example:
The polynomial that has the reciprocal roots of the original, is another method that can be used when a zero appears only in the first column of a row.
(s is replaced by l/d),
reciprocal roots
Since there are two sign changes, the system is unstable and has two right-half-plane poles

## Slide 28
Routh-Hurwitz Criterion: Special Cases
2. Entire Row is Zero
Stable system.
An entire row consists of zeros because there is an even polynomial that is a factor of the original polynomial (only even powers of s and have roots that are symmetrical about the origin.)
Example:
the row was multiplied by 1/7
entire row consists of zeros
Derivative of the polynomial of the row above the zeros row

## Slide 29
Pole Distribution via Routh Table with Row of Zeros
:Even polynomial
No sign change
Two sign changes
entire row consists of zeros
the row was multiplied by 1/10
the row was multiplied by 1/20
the row was multiplied by 1/2
PROBLEM:
Tell how many poles are in the right half-plane, in the left half-plane, and on the jw-axis.
Taking the derivative
interpretation

## Slide 30
Stability Design via Routh-Hurwitz
1. If K < 1386, then stable system.
2. If K > 1386, then two sign changes; two right-half plane poles and one left-half plane pole. Unstable system.
3. If K = 1386, an entire row of zeros  j poles.
No sign change
2 poles in j axis and one left-half plane pole
Changes in the gain K of a feedback control system change the closed-loop pole locations (can move poles from region to another region on the S-plane).
PROBLEM:
Find the range of gain, K, for the system that will cause the system to be stable, unstable, and marginally stable. Assume K > 0.
can be positive, zero, or negative
Variable gain K
Row of zeros
replacing K=1386
the system is marginally stable
no sign changes above the even polynomial

## Slide 31
Factoring via Routh-Hurwitz
Factor the polynomial
The Routh-Hurwitz criterion is often used in limited applications to factor polynomials containing even factors.
PROBLEM:
Dividing polynomial (1) by (2) yields:
(1)
(2)

## Slide 32
Stability in State Space
Unstable system.
The values of the system's poles are equal to the eigenvalues of the system matrix, A.
PROBLEM: find out how many poles are in the left half-plane, in the right half-plane, and on the jw-axis.
SOLUTION:
Using this polynomial, form the Routh table
one sign change: One right-half-plane pole and two left-half-plane poles.

## Slide 33
3. Steady-State Errors
Steady-State Error: The difference between the input and the output for a prescribed test input (step / ramp / parabola) as t 
Steady-state error
step input
ramp input
Test waveforms for evaluating steady-state errors of position control systems

## Slide 34
Evaluating Steady-State Errors1
Applying final value theorem
Problem: Find the steady-state error for the following system with
and input is step response.
Solution:
T(s) is stable, hence E(s) is stable.
Applying final value theorem,
Closed-loop control system error
input
output
Error
Step input
We have the error

## Slide 35
Evaluating Steady-State Errors2
[Final-value theorem]
Step input: u(t)
For zero steady-state error,
Ramp input: tu(t)
For zero steady-state error,
Parabolic input: (1/2)t2u(t)
For zero steady-state error,

## Slide 36
Evaluating Steady-State Errors example1
Problem:
Find steady-state errors for inputs 5u(t), 5tu(t), and 5t2u(t) to the above system.
Solution:
u(t): unity step
Let, the system is stable.

## Slide 37
Evaluating Steady-State Errors-example2
One integration, s1
Two integrations will make it constant and 3 or more will make it zero.
No integration will make it infinity.
one integration makes it constant.
No integration will make it constant,
one integration makes it zero.

## Slide 38
Static Error Constants
Position constant, Kp:
Velocity constant, Kv:
Acceleration constant, Ka:
The steady-state error performance specifications are called static error constants.
steady-state error.
step input, u(t)
ramp input, t u(t)
PROBLEM:
evaluate the static error constants and find the expected error for the standard step, ramp, and parabolic inputs.

## Slide 39
System Type
Type 0: if n = 0; (no integration)
Type 1: if n = 1; (one integration)
Type 2: if n = 2; (two integrations)
Problem:
Solution:
Find the value of K so that there is 10% error in the steady state.
Type 1.
Input should be ramp, because only ramp yields a finite error in Type 1 system.

## Slide 40
Relationships between input, system type, static error constants, and steady-state errors
System Type

## Slide 41
Steady-State Error for Disturbances
Feedback control systems are used to compensate for disturbances or unwanted inputs that enter a system.
disturbance
steady-state error due to R(s),
steady-state error due to disturbance D(s),
steady-state error due to step disturbance D(s)=1/s,
Problem:
Find the steady-state error component due to a step disturbance
Solution:

## Slide 42
Steady-State Error for Nonunity Feedback System
Type 0 (as no integration).
For step input, static error constant is Kp.
Negative value means the output step is larger than the input step.
Form a unity feedback system by adding and subtracting unity feedback paths (input and output units must be same.).
PROBLEM:
Find the system type, error constant, and the steady-state error for a unit step input.