## Slide 1: Chapter 12
Concrete Construction
Part 1

## Slide 2: Chapter 12: Concrete Construction
12-1 CONSTRUCTION APPLICATIONS OF CONCRETE
12-2 CONCRETE CONSTRUCTION PRACTICES
12-3 CONCRETE FORMWORK
12-4 REINFORCING STEEL
12-5 QUALITY CONTROL

## Slide 3: 12-1 CONSTRUCTION APPLICATIONS OF CONCRETE
Concrete, or more properly portland cement concrete, is one of the world's most versatile and widely used construction materials.
construction applications:
  paving of highways and airfields.
  its use in foundations for small structures, through structural components such as beams, columns, and wall panels, to massive concrete dams.
all concrete used for structural purposes contains reinforcing steel embedded in the concrete to increase the concrete member's tensile strength. (Reinforced Concrete)

## Slide 4: 12-1 CONSTRUCTION APPLICATIONS OF CONCRETE
The objective of the construction manager should be to develop a construction plan which minimizes construction costs while meeting all safety and quality requirements.
Major elements of a concrete construction cost analysis include:
  Formwork costs including labor, equipment, and materials.
  Cost of reinforcing steel and its placement.
  Concrete materials, equipment, and labor for placing, curing, and finishing the concrete.

## Slide 5: FIGURE 12-1: Typical distribution of concrete construction costs.

## Slide 6: 12-1 CONSTRUCTION APPLICATIONS OF CONCRETE
1. Cast-in-Place Concrete
2. Precast Concrete
3. Prestressed Concrete
4. Architectural Concrete

## Slide 7: 1. Cast-in-Place Concrete
Concrete structural members have traditionally been built in-place by placing the plastic concrete into forms and allowing it to harden.
The forms are removed after the concrete has developed sufficient strength to support its own weight and the weight of any construction loads.

## Slide 8: FIGURE 12-2: Typical cast-in-place column and wall shapes.

## Slide 9: FIGURE 12-3: Pumping concrete into bottom of column form. (Courtesy of Gates & Sons, Inc.)

## Slide 10: FIGURE 12-4: Floor slab construction. (Courtesy of Concrete Reinforcing Steel Institute)

## Slide 11: FIGURE 12-5: Waffle slab. (Courtesy of Concrete Reinforcing Steel Institute)

## Slide 12: FIGURE 12-6: Flat slab and flat plate slab. (Courtesy of Concrete Reinforcing Steel Institute)

## Slide 13: 2. Precast Concrete
Precast concrete is concrete that has been cast into the desired shape prior to placement in a structure.
There are a number of advantages obtained by removing the concrete forming, placing, finishing, and curing operations from the construction environment.
Pre-casting operations usually take place in a central plant where industrial production techniques may be used.
Since standard shapes are commonly used, the repetitive use of formwork permits forms to be of high quality at a low cost per unit.

## Slide 14: Precast Concrete
There are a number of standard shapes commonly used for precast concrete structural members.
Figure 12-7 illustrates some common beam and girder sections.
Figure 12-8 illustrates Precast roof and floor panels.

## Slide 15: FIGURE 12-7: Precast beam and girder shapes.

## Slide 16: FIGURE 12-8: Precast slab shapes.

## Slide 17: FIGURE 12-9: Steps in tilt-up construction. (Courtesy of The Burke Company)

## Slide 18: FIGURE 12-9: Steps in tilt-up construction. (Courtesy of The Burke Company)

## Slide 19: 3. Prestressed Concrete
Prestressed concrete is concrete to which an initial compression load has been applied.
Prestressing serves to increase the load that a beam or other flexural member can carry before allowable tensile stresses are reached.
  because the concrete is quite strong in compression but weak in tension,

## Slide 20: FIGURE 12-10: Stresses in a Prestressed simple beam.

## Slide 21: Prestressed Concrete
Advantages:
  permits a smaller, lighter member to be used in supporting a given load.
  reduces the amount of deflection in a beam.
  Since the member is always kept under compression, any cracking that does occur will remain closed up and not be apparent.

## Slide 22: Prestressed Concrete
Disadvantages:
  higher material, equipment, and labor cost involved in the production of prestressed components.

## Slide 23: Prestressed Concrete
There are two methods for producing prestress in concrete members;
  pretensioning and
  posttensioning.

## Slide 24: Prestressed Concrete
Caution must be observed in handling and transporting pretensioned prestressed members, particularly if they are asymmetrically stressed.
FIGURE 12-11: Lifting prestressed beam at the center.
It should be lifted by the ends or by using multiple lift points along the beam.

## Slide 25: 4. Architectural Concrete
The architectural use of concrete to provide appearance effects has greatly increased in recent years.
Architectural effects are achieved by the shape, size, texture, and color used.

## Slide 26: FIGURE 12-12: Application of architectural concrete. (Courtesy of Portland Cement Association)

## Slide 27: Architectural Concrete
Some of the major methods used for obtaining architectural concrete effects include:
  exposed aggregate surfaces (Figure 12-13a),
  special surface designs and textures achieved by the use of form liners (Figure 12-13b), and
  mechanically produced surfaces (Figure 12-14).
Exposed aggregate surfaces are produced by removing the cement paste from the exterior surface, exposing the underlying aggregate.

## Slide 28: FIGURE 12-13: Architectural concrete surfaces. (Courtesy of Portland Cement Association)

## Slide 29: FIGURE 12-14: Mechanically produced concrete surface texture. (Courtesy of Portland Cement Association)