## Slide 1: PPP Protocol

## Slide 2: Outline
Serial Communication
Point-to-Point Communication Links
HDLC Encapsulation
Point-to-Point Protocol (PPP)
  PPP components
  Establishing a PPP Session
  PPP Authentication Protocols
  PPP Configuration
  Configuring PPP Authentication

## Slide 3: Introduction to WANs
WAN Connection Options

## Slide 4: Serial and Parallel Ports
Communications across a serial connection is a method of data transmissions in which the bits are transmitted sequentially over a single channel.
In parallel communications, bits can be transmitted simultaneously over multiple wires.
Notes: 3.1.1.1 Serial and Parallel Ports

## Slide 5: Serial Communications Serial Communication
On the WAN link, data is encapsulated by the protocol used by the sending router.
Encapsulated frame is sent on a physical medium to the WAN.
Receiving router uses the same communications protocol to de-encapsulate the frame when it arrives.
Three serial communication standards for LAN-to-WAN connections: RS-232, V.35, HSSI
Notes: 3.1.1.2 Serial Communication

## Slide 6: WAN Connection Types
WAN Data Link
Protocolos

## Slide 7: Serial Communications Point-to-Point Communication Links
Point-to-point links can connect two geographically distant sites.
Point-to-point connections are used to connect LANs to service provider WANs.
  Also referred to as a serial connection or leased-line connection
Carrier dedicates specific resources for a line leased by the customer (leased-line).
Point-to-point links are usually more expensive than shared services.
Notes: 3.1.1.3 Point-to-Point Communication Links

## Slide 8: HDLC Encapsulation HDLC Encapsulation
A data link layer protocol developed by the International Organization for Standardization (ISO) . (standard HDLC)
Defines a Layer 2 framing structure
Cisco has developed an extension to the HLDC protocol to solve the inability to provide multiprotocol support (Cisco HLDC also referred to as cHDLC).
Notes: 3.1.2.2 HDLC Encapsulation

## Slide 9: HDLC Encapsulation
HDLC defines a Layer 2 framing structure

## Slide 10: HDLC Encapsulation
Standard HDLC
  does not support multiple protocols on a single link, as it does not have a way to indicate which protocol is being carried.
Cisco HDLC
  The frame uses a ‘protocol' field that enables multiple network layer protocols to share the same serial link.

## Slide 11: HDLC Encapsulation HDLC Encapsulation
Default encapsulation method used by Cisco devices on synchronous serial lines
Point-to-point protocol on leased lines between two Cisco devices
Connecting to a non-Cisco device, use synchronous PPP

## Slide 12: HDLC Encapsulation Configuring HDLC Encapsulation
Notes: 3.1.2.4 Configuring HDLC Encapsulation

## Slide 13: Point-to-Point Protocol (PPP)
  Point-to-Point Protocol (PPP) is also data link protocol used on serial links just like HDLC.
  However PPP is has more advanced features when compared with HDLC which is quite primitive. For example:
    Link quality management feature monitors the quality of the link. If too many errors are detected, PPP takes down the link
    Supports PAP and CHAP authentication

## Slide 14: Benefits of PPP Introducing PPP
PPP contains three main components:
  HDLC protocol for encapsulating datagrams over point-to-point links
  Extensible Link Control Protocol (LCP) to establish, configure, and test the data link connection
  Family of Network Control Protocols (NCPs) to establish and configure different network layer protocols (IPv4, IPv6, AppleTalk, Novell IPX, and SNA Control Protocol)
Notes: 3.2.1.1 Introducing PPP

## Slide 15: LCP and NCP PPP Layered Architecture
  LCP sets up the PPP connection and its parameters and terminates it
  NCPs handle higher layer protocol configurations
Notes: 3.2.2.1 PPP Layered Architecture

## Slide 16: LCP and NCP PPP Control Protocol (LCP)
  PPP uses the LCP to negotiate and setup control options on the WAN link.
  Authentication, Compression, Error Detection, Multilink for load balancing, and link monitoring functions.
Notes: 3.2.2.2 PPP – Link Control Protocol (LCP)

## Slide 17: LCP and NCP PPP Network Control Protocol (NCP)
  PPP permits multiple network layer protocols to operate on the same communications link.
  For every network layer protocol used, PPP uses a separate NCP.
Notes: 3.2.2.3 PPP – Network Control Protocol (NCP)

## Slide 18: PPP Sessions Establishing a PPP Session
  Phase 1 – LCP must first open the connection and negotiate configuration options;
Notes: 3.2.3.1 Establishing a PPP Session

## Slide 19: PPP Sessions PPP Configuration Options
Optional functions include:
  Authentication using either PAP or CHAP
  Compression using either Stacker or Predictor
  Multilink that combines two or more channels to increase the WAN bandwidth
Notes: 3.2.3.4 PPP Configuration Options

## Slide 20: Configure PPP PPP Configuration Options
  Authentication – Two authentication choices are Password Authentication Protocol (PAP) and Challenge Handshake Authentication Protocol (CHAP).
  Compression – Increases the effective throughput on PPP connections by reducing the amount of data in the frame that must travel across the link. The protocol decompresses the frame at its destination. Two compression protocols available in Cisco routers are Stacker and Predictor.
  Multilink – This alternative provides load balancing over the router interfaces that PPP uses. Multilink PPP provides a method for spreading traffic across multiple physical WAN links while providing packet fragmentation and reassembly, proper sequencing, multivendor interoperability, and load balancing on inbound and outbound traffic.
Notes: 3.3.1.1 PPP Configuration Options

## Slide 21: PPP Sessions Establishing a PPP Session (cont.)
Phase 2 –Authentication Phase
After the link has been established and the authentication protocol decided on, the peer may be authenticated.
Authentication, if used, takes place before the network layer protocol phase is entered.
PPP uses PAP and CHAP as authentication protocols
As part of this phase, LCP also allows for an optional link-quality determination test.
  The link is tested to determine whether the link quality is good enough to bring up network layer protocols.
Notes: 3.2.3.1 Establishing a PPP Session

## Slide 22: PPP Sessions Establishing a PPP Session (cont.)
Phase 3 – Network Layer Protocol Phase.
In this phase the PPP devices send NCP packets to choose and configure one or more network layer protocols, such as IP.
Once each of the chosen network layer protocols has been configured, packets from each network layer protocol can be sent over the link.
Notes: 3.2.3.1 Establishing a PPP Session

## Slide 23: Configure PPP PPP Basic Configuration Command
Notes: 3.3.1.2 PPP Basic Configuration Command

## Slide 24: Configure PPP Verifying PPP Configuration
Notes: 3.3.1.6 Verifying PPP Configuration

## Slide 25: PPP Authentication PPP Authentication Protocols
Notes: 3.3.2.1 PPP Authentication Protocols

## Slide 26: PPP Authentication Password Authentication Protocol (PAP)
Initiating PAP
Completing PAP
Notes: 3.3.2.2 Password Authentication Protocol (PAP)

## Slide 27: Password Authentication Protocol (PAP)
PAP provides a simple method for a remote node to establish its identity, using a two-way handshake.
The authentication process is one way authentication method and one or both devices can authenticate each other separately.
PAP is not a strong authentication protocol.
Passwords are sent across the link in clear text and there is no protection from playback or repeated trial-and-error attacks.
Notes: After the PPP link establishment phase is complete, a username/password pair is repeatedly sent by the remote node across the link until authentication is acknowledged or the connection is terminated.

## Slide 28: PPP Authentication Challenge Handshake Authentication Protocol
Initiating CHAP
Responding CHAP
Notes: 3.3.2.3 Challenge Handshake Authentication Protocol (CHAP)

## Slide 29: PPP Authentication CHAP (cont.)
Completing CHAP
Notes: 3.3.2.3 Challenge Handshake Authentication Protocol (CHAP)

## Slide 30: CHAP
CHAP uses a three-way handshake to verify the identity of the remote node.
After the PPP link establishment phase is complete, the local router sends a "challenge" message to the remote node.
The remote node responds with a value calculated using a one-way hash function, which is typically Message Digest 5 (MD5).
This response is based on the password and challenge message.
The local router checks the response against its own calculation of the expected hash value.
If the values match, the authentication is acknowledged, otherwise the connection is immediately terminated.

## Slide 31: CHAP
CHAP provides protection against playback attack through the use of a variable challenge value that is unique and unpredictable.
Since the challenge is unique and random, the resulting hash value will also be unique and random.

## Slide 32: PPP Authentication Configuring PPP Authentication (cont.)
Notes: 3.3.2.6 Configuring PPP with Authentication

## Slide 33: PPP Authentication Configuring PPP Authentication (cont.)
Notes: 3.3.2.6 Configuring PPP with Authentication