## Slide 1
KING SAUD UNIVERSITY COLLEGE OF APPLIED STUDIES AND COMMUNITY SERVICE |  | 
CT 1402 | Lab sheet #3 | 1nd semester 1438-1439
By: Adal ALashban |  | 
Delta Modulation

## Slide 2: Introduction
Delta modulation (DM) is an analog-to-digital signal conversion technique used for transmission of voice information where quality is not of primary importance.
PCM finds the value of the signal amplitude for each sample; DM finds the change from the previous sample.

## Slide 3: Basic Operation
The operation of a delta modulator is:
  to periodically sample the input message,
  to make a comparison of the current sample with that preceding it,
  and to output a single bit which indicates the sign of the difference between the two samples

## Slide 4: Delta Modulation
In Delta Modulation, only one bit is transmitted per sample
That bit is a 1 if the current sample is more positive than the previous sample, and a 0 if it is more negative
Since so little information is transmitted, delta modulation requires higher sampling rates than PCM for equal quality of reproduction

## Slide 5: Delta Modulation
1- A staircase approximation of the message signal is derived
  The analog signal is approximated with a series of segments ( staircase approximation signal)
  Each segment of the approximated signal is compared to the message signal:
      If the approximation fall below the signal at any sampling epoch  the segment is increased by ∆.
      If the approximation lies above the signal at any sampling epoch  the segment is diminished by ∆.
  So, the time and amplitude axes are quantized.

## Slide 7: Delta Modulation
2- encoding
This scheme sends only one bit each segment.
  if the segment at time tn+1 is higher in amplitude value than the segment at time tn,  then a bit “1” is used to indicate the positive value.
  If the segment is lower in value  resulting in a negative value, a “0” is used.

## Slide 8
This scheme works well for small changes in signal values between samples.
If changes in amplitude are large, this will result in large errors.

## Slide 9: :DM Using Simulink

## Slide 11
If there is no sample time option; can be add by following:
1- right click then choose  Explore

## Slide 12
2- If there is no sample time here;  Choose show details

## Slide 13
3- Then add sample time

## Slide 14
4- Then add value in sample time

## Slide 18
Using a Matlab program to simulate a Delta Modulation modulator with demodulator?
Signal generator block(Amplitude "3", frequency "15 Hz"), Pulse generator block(period "1").

## Slide 20
Thank You