## Slide 1
Data Transmission And Digital Communication
Lecture 1– 2019/1440
By: Elham Sunbu

## Slide 2: OUTLINE
Matlab introduction
Why Matlab
Matlab Software install and interface

## Slide 3: Layered Tasks
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.

## Slide 4: Figure: Tasks involved in sending a letter

## Slide 5: Note:
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
THE OSI MODEL
ISO is the organization.
OSI is the model.

## Slide 6: Figure: The interaction between layers in the OSI model

## Slide 7: Figure: An exchange using the OSI model

## Slide 8: LAYERS IN THE OSI MODEL
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
In this section, we briefly describe the functions of each layer in the OSI model.

## Slide 9: Physical Datalink Network Transport Session Presentation Application
Application Layer
  set of utilities used by application programs
Presentation Layer
  formats data for presentation to the user
  provides data interfaces, data compression and translation between different data formats
Session Layer
  initiates, maintains and terminates each logical session between sender and receiver
7-LAYER MODEL OF OSI |  |  |  |  |  | 

## Slide 10: Physical Datalink Network Transport Session Presentation Application
Transport Layer
  deals with end-to-end issues such as segmenting the message for network transport, and maintaining the logical connections between sender and receiver
Network Layer
  responsible for making routing decisions
Data Link Layer
  deals with message delineation, error control and network medium access control
Physical Layer
  defines how individual bits are formatted to be transmitted through the network
7-LAYER MODEL OF OSI |  |  |  |  |  | 

## Slide 11: Figure: Summary of layers

## Slide 12: Physical Datalink Network Transport Application
1 -
12
Application Layer
  used by application program
Transport Layer
  responsible for establishing end-to-end connections, translates domain names into numeric addresses and segments messages
Network Layer - same as in OSI model
Data Link Layer - same as in OSI model
Physical Layer - same as in OSI model
INTERNET’S 5-LAYER MODEL |  |  |  | 

## Slide 13: COMPARISON OF NETWORK MODELS
1 -
13

## Slide 14: MESSAGE TRANSMISSION USING LAYERS
1 -
14
Applications A
pplications
sender receiver
A receiving layer wraps incoming message with an envelope
Adds layer related addressing
information
A receiving layer removes the layer related envelope and
forwards the
message up

## Slide 15
DATA VERSUS SIGNAL
Data | Signals
Convey meaning within a computer (stored in files). | Electric or electromagnetic encoding of data.
Need to be converted into a signal before transfer. | Networks and communication systems transmit signals.
can be analog ( information can be audio or video) or digital (binary) | 
 | Issues related to the transmission of signals: Impairments (also transmission flaws) Capacity of the media

## Slide 16
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data
A COMMUNICATIONS MODEL

## Slide 17
Transmission system utilization | Addressing
Interfacing | Routing
Signal generation | Recovery
Synchronization | Message formatting
Exchange management | Security
Error detection and correction | Network management
Flow control | 
COMMUNICATIONS TASKS

## Slide 18: SIMPLIFIED COMMUNICATIONS MODEL - DIAGRAM

## Slide 19: SIMPLIFIED DATA COMMUNICATIONS MODEL

## Slide 20: Figure: Data flow (simplex, half-duplex, and full-duplex)

## Slide 21
Analog signals
  Value varies continuously
Digital signals
  Value limited to a finite set
Binary signals
  Has at most 2 values
  Used to represent bit values
  Bit time T needed to send 1 bit
  Data rate R=1/T bits per second
t
x(t)
t
x(t)
t
x(t)
1
0 0 0
1
1
0
T
Analog vs. Digital

## Slide 22
Time domain (examining the signal over time):
  Continuous signal - signal with no breaks or discontinuities
  Discrete signal - signal with a finite number of values
  Amplitude - the instantaneous value of a signal (Volt)
  Frequency - inverse of the period in cycles per second, Hertz
  Phase - measure of relative position in time within a single period (degree or radian)
Frequency, Spectrum and Bandwidth

## Slide 23
Frequency Domain (signal viewed as a function of frequency):
  any signal is made up of components at various frequencies, each sinusoid
Spectrum- the range of frequencies in a signal
Absolute bandwidth - is the width of the spectrum (fn - f1) where, fn is largest frequency in signal and f1 is the smallest
Audio signal
Digital signal
Frequency, Spectrum and Bandwidth

## Slide 24: Modulation and Encoding schemes
Modulation:
Encoding:

## Slide 25: Conversion
Encoding | Modulation
Digital data to digital signal : less complex and less expensive equipment than analog modulation equipment. | Digital data to analog signal : Some transmission media can propagate analog signals only. Example: fiber , wire.
Analog data to digital signal : To use the modern digital transmission and switching equipment. Transmit baseband signal over wire transmission (Microwave) => Low frequency baseband means few kilometer antenna !!! shift baseband signals of several voice channel (FDM). | 

## Slide 26: Figure: Transmission medium and physical layer

## Slide 27: Figure: Classes of transmission media

## Slide 28
GUIDED MEDIA
Guided media, which are those that provide a conduit from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable.
Topics discussed in this section:
  Twisted-Pair Cable
  Coaxial Cable
  Fiber-Optic Cable

## Slide 29: Figure: Twisted-pair cable

## Slide 30
Figure :UTP and STP cables

## Slide 31: Figure :UTP connector

## Slide 32: Figure : Coaxial cable

## Slide 33: Categories of coaxial cables

## Slide 34
Figure: Optical fiber

## Slide 35
Figure Propagation modes

## Slide 36
Figure : Modes

## Slide 37
Figure: Fiber construction

## Slide 38
UNGUIDED MEDIA: WIRELESS
Unguided media transport electromagnetic waves without using a physical conductor.
This type of communication is often referred to as wireless communication.

## Slide 39
Figure :Wireless transmission waves

## Slide 40
Thank You