## Slide 1: Lecture 2 Transmission Basics

## Slide 2: Data vs Signal
Data – information formatted in human/machine readable form
  examples: voice, music, image, file
Signal – electric or electromagnetic representation of data
  transmission media work by conducting energy along a physical path; data must be turned into energy in the form of electro-magnetic signals to be transmitted

## Slide 3: Transmission Basics
Transmission – communication of data through propagation and processing of signals
Transmit means to issue signals to the network medium
Transmission refers to either the process of transmitting or the progress of signals after they have been transmitted

## Slide 4: Terminology (1)
Data transmission occurs between transmitter and receiver over some transmission medium.
Signal: electromagnetic waves
  Can propagate along the transmission medium
Transmission Medium
  Guided medium: the signals are guided along a physical path
    e.g., twisted pair, coaxial cable, optical fiber
  Unguided medium: wireless
    e.g., air, water, vacuum

## Slide 5: Terminology (2)
Direct link
  Refer to the transmission path between the transmitter and receiver in which signals propagate directly with no intermediate devices, other than amplifiers or repeaters used to increase signal strength.
  Note that it can apply to both guided and unguided media
A transmission medium is point-to-point if:
  Direct link
  Only 2 devices share the medium
A transmission medium is multipoint if:
  More than two devices share the same medium
Point-to-point
Multipoint

## Slide 6: Analog and Digital Signals

## Slide 7: Transmission Basics
Analog and Digital Signaling
  On a data network, information can be transmitted via one of two signaling methods: analog or digital
    Both types of signals are generated by electrical current, the pressure of which is measured in volts

## Slide 8: Transmission Basics (continued)
An analog signal, like other waveforms, is characterized by four fundamental properties:
  Amplitude
  Frequency
  Wave length
  Phase

## Slide 9: Analog Signals
Amplitude:
  Analog wave’s strength
  Amplitude of a signal refers to the height of the signal.
Frequency:
  frequency refers to number cycles per second.
  Measure in hertz (Hz)
Wavelength:
  Distance between corresponding wave cycle points
  Inversely proportional to frequency
  Expressed in meters or feet

## Slide 10: Analog Signals
Phase
  Phase describes the position of the waveform relative to time zero.
  Phase is measured in degrees
    phase shift of 90º = shift of ¼ cycle
    phase shift of 180º = shift of ½ cycle
    Phase shift of 270 – shift of ¾ cycle

## Slide 11
Two signals with the same amplitude and phase, but different frequencies

## Slide 12
Two signals with the same phase and frequency, but different amplitudes

## Slide 13
Three sine waves with the same amplitude and frequency, but different phases

## Slide 14: Analog Signals
Analog signal benefit over digital
  More variable
  Convey greater subtleties with less energy
Drawback of analog signals
  Varied and imprecise voltage
  Vulnerable to transmission flaws

## Slide 15: Digital Signals
Digital signals
  Pulses of voltages
  Positive voltage represents a 1
  Zero voltage represents a 0
Digital signals composed of pulses
bit interval – time required to send a single bit, unit: [sec]
bit rate – number of bit intervals per second – unit: [bps]

## Slide 16: Bandwidth and Bitrate
Bandwidth - The amount of data that can be transmitted in a fixed amount of time.
For digital devices, the bandwidth is usually expressed in bits per second (bps) or bytes per second.
For analog devices, the bandwidth is expressed in cycles per second, or Hertz (Hz).
Bitrate - is the number of transmitted bits per time unit (usually seconds) expressed in bits per second (bps) or bytes per second. Bit rate is part of bandwidth.

## Slide 17: Data and Signals
Usually use digital signals for digital data and analog signals for analog data
Can use analog signal to carry digital data
  Modem
Can use digital signal to carry analog data
  Compact Disc audio

## Slide 18: Analog Signals Carrying Analog and Digital Data

## Slide 19: Digital Signals Carrying Analog and Digital Data

## Slide 20: Analog Transmission
Analog signal transmitted without regard to content
May be analog or digital data
Attenuated over distance
Use amplifiers to boost signal
Also amplifies noise

## Slide 21: Digital Transmission
Concerned with content
Integrity endangered by noise, attenuation etc.
Repeaters used
Repeater receives signal
Extracts bit pattern
Retransmits
Attenuation is overcome
Noise is not amplified

## Slide 22: Advantages of Digital Transmission
Digital technology
  Low cost technology
Data integrity
  Longer distances over lower quality lines
Capacity utilization
  High bandwidth links economical
  High degree of multiplexing easier with digital techniques
Security & Privacy
  Encryption
Integration
  Can treat analog and digital data similarly

## Slide 23: Transmission Impairment

## Slide 24: Transmission Impairments
With any communications system, the signal that is received may differ from the signal that is transmitted, due to various transmission impairments.
Consequences:
  For analog signals: degradation of signal quality
  For digital signals: bit errors
The most significant impairments include
  Attenuation
  Distortion
  Noise

## Slide 25: Attenuation
It means loss of energy.
The strength of signal decreases with increasing distance which causes loss of energy in overcoming resistance of medium.
Amplifiers are used to amplify the attenuated signal which gives the original signal back.

## Slide 26: Attenuation
Attenuation is measured with decibel (dB) .
Decibel: A measure of the relative strength of two signal points.
Decibel can be positive + is signal is amplified, or negative if signal is attenuated.

## Slide 27: decibel
dB = 10 Log10 ( P2/P1)
  P2: the power of a signal at the end point (Watt)
  P1: the power of a signal at the start point (Watt).
Example1:
Imagine a signal travels through a transmission medium and its power is reduced to half. Calculate the decibel.
  Reduced to half means P2 = ½ P1
  dB = 10 Log10 (P2/P1) = 10 Log 10 (0.5 p1/p1)
  dB = 10 Log 10 (0.5) = 10 (-0.3) = - 3 dB

## Slide 28: Distortion
It means change in the shape of signal.

## Slide 29: Noise
For any data transmission event, the received signal will consist of the transmitted signal, modified by the various distortions imposed by the transmission system, plus additional unwanted signals that are inserted somewhere between transmission and reception.
The undesired signals are referred to as noise, which is the major limiting factor in communications system performance.
Four categories of noise:
  Thermal noise
  Intermodulation noise
  Crosstalk
  Impulse noise

## Slide 30: Noise
Thermal noise (or white noise)
  Due to thermal agitation of electrons
  It is present in all electronic devices and transmission media, and is a function of temperature.
  Cannot be eliminated, and therefore places an upper bound on communications system performance.
Intermodulation noise
  When signals at different frequencies share the same transmission medium, the result may be intermodulation noise.
  Signals at a frequency that is the sum or difference of original frequencies or multiples of those frequencies will be produced.

## Slide 31: Noise
Crosstalk
  It is an unwanted coupling between signal paths. It can occur by electrical coupling between nearby twisted pairs.
  Typically, crosstalk is of the same order of magnitude as, or less than, thermal noise.
Impulse noise
  Impulse noise is non-continuous, consisting of irregular pulses or noise spikes of short duration and of relatively high amplitude.
  It is generated from a variety of cause, e.g., external electromagnetic disturbances such as lightning.
  It is generally only a minor annoyance for analog data.
  But it is the primary source of error in digital data communication.

## Slide 32: Modulation

## Slide 33: Modulation
Modulation
  Modulation is the process of encoding information from a message source in a way that is suitable for transmission.
  Modulation technique is used to change the signal characteristics.
Why do we modulate
  larger distance transfer
  accurate data transfer
  low-noise data reception

## Slide 34: Modulation

## Slide 35: Analog Modulation
Analog modulation: a continuously varying sine wave is used as a carrier wave that modulates the message signal or data signal.

## Slide 36: Amplitude Modulation
Amplitude modulation or AM: the height of the signal carrier is varied to represent the data being added to the signal.
The other factors like phase and frequency remain constant.

## Slide 37: Frequency Modulation
Frequency modulation (FM), in which the frequency of the carrier waveform is varied to reflect the frequency of the data.
The other factors like phase and amplitude remain constant.

## Slide 38: Phase Modulation
Phase modulation (PM), in which the frequency of the carrier waveform is varied to reflect changes in the frequency of the data.
it affects the frequency. So, for this reason, this modulation is also comes under the frequency modulation.

## Slide 39: Analog Modulation
Analog modulation (AM, FM and PM) is more sensitive to noise. If noise enters into a system, it persists and gets carried till the end receiver. Therefore, this drawback can be overcome by the digital modulation technique.

## Slide 40: Digital modulation
Digital modulation modifies an analog carrier signal with another discrete signal.
For a better quality and efficient communication, digital modulation technique is employed.
The main advantages of the digital modulation over analog modulation:
  permissible power,
  available bandwidth and
  high noise immunity.
In digital modulation, a message signal is converted from analog to digital message, and then modulated by using a carrier wave.

## Slide 41: Digital Modulation
In an Amplitude shift keying ASK, the amplitude of the carrier wave changes based on the message signal or on the base-band signal, which is in digital format.
It is sensitive to noise and used for low-band requirements.
In Frequency Shift Keying FSK, the frequency of the carrier wave is varied for each symbol in the digital data.
It needs larger bandwidths.
The Phase Shift Keying PSK changes the phase of the carrier for each symbol.
It is less sensitive to noise.

## Slide 42: Transmission Types

## Slide 43: Transmission Types
Simplex transmission
  Signals are transmitted in only one direction
    e.g. Television
Half duplex
  Signals can be transmitted in either direction, but only one way at a time.
    e.g. police radio
Full duplex
  Both stations may transmit simultaneously.
    e.g. telephone

## Slide 44: Transmission Basics (continued)
Multiplexing
  Allows multiple signals to travel simultaneously over one medium
  In order to carry multiple signals, the medium’s channel is logically separated into multiple smaller channels, or sub channels
  A device that can combine many signals on a channel, a multiplexer (mux), is required at the sending end of the channel
  At the receiving end, a demultiplexer (demux) separates the combined signals and regenerates them in their original form

## Slide 45: Multiplexing

## Slide 46
Categories of multiplexing

## Slide 47: Frequency Division Multiplexing
FDM
Useful bandwidth of medium exceeds required bandwidth of channel
Each signal is modulated to a different carrier frequency
Carrier frequencies separated so signals do not overlap (guard bands)
e.g. broadcast radio
Channel allocated even if no data

## Slide 48
Frequency-division multiplexing (FDM)

## Slide 49
FDM process

## Slide 50
FDM demultiplexing example

## Slide 51: Time Division Multiplexing (TDM)
Two ways of implementing TDM are:
  Synchronous TDM
  Asynchronous TDM

## Slide 52: Synchronous TDM
Synchronous TDM works by the muliplexor giving exactly the same amount of time to each device connected to it.
This time slice is allocated even if a device has nothing to transmit.
This is wasteful in that there will be many times when allocated time slots are not being used.
Therefore, the use of Synchronous TDM does not guarantee maximum line usage and efficiency.

## Slide 53
Synchronous time-division multiplexing

## Slide 54: Asynchronous TDM
Asynchronous TDM is a more flexible method of TDM. With Asynchronous TDM the length of time allocated is not fixed for each device but time is given to devices that have data to transmit.
This version of TDM works by tagging each frame with an identification number to note which device it belongs to.
This may require more processing by the multiplexor and take longer, however, the time saved by efficient and effective bandwidth utilization makes it worthwhile.