## Slide 1: Lecture 3: Wireless Sensor Networks
By: Dr. Najla Al-Nabhan

## Slide 2: Wireless Sensor Networks (WSNs)
A sensor network is a wireless network that consists of thousands of very small nodes called sensors.
Base station
Figure 1: Architecture of wireless sensor networks
Notes: - (WSN) stands for wireless sensor network.
- This technology involves deploying a large #number of inexpensive/small sensor nodes over the area of interest
- The main function of sensor nodes is to monitor, record, and notify a specific condition to the BS
- The collected data is transferred to the BS in multi-hop fashion from one node to another using broadcast communication.

## Slide 3: Wireless Sensor Networks (cont.)
WSN Sensors are equipped with sensing, limited computation, and wireless communication capabilities.
Figure 2: Typical hardware components of a sensor node in wireless sensor networks
Notes: Sensors are mainly equipped with:
A sensing unit: to sense the environmental parameters
A microcontroller to perform the local data processing
A wireless communication unit that allows node to communicate with other nodes, and
A Power Unit or a battery: that empowers all components of the sensor node.

## Slide 4: Introduction
Wireless Sensor Networks are networks that consists of sensors which are distributed in an ad hoc manner.
These sensors work with each other to sense some physical phenomenon and then the information gathered is processed to get relevant results.
Wireless sensor networks consists of protocols and algorithms with self-organizing capabilities.

## Slide 5: Comparison with ad hoc networks
  Wireless sensor networks mainly use broadcast communication while ad hoc networks use point-to-point communication.
  Unlike ad hoc networks wireless sensor networks are limited by sensors limited power, energy and computational capability.
  Sensor nodes may not have global ID because of the large amount of overhead and large number of sensors.

## Slide 6: WSNs Applications
WSNs have many advantages over traditional networking techniques.
They have an ever-increasing number of applications, such as infrastructure protection and security, surveillance, health-care, environment monitoring, food safety, intelligent transportation, and smart energy.
Notes: There are many challenges related to this class of networks, such as
limited resources of sensor nodes
networking challenges
how to perform routing and multihop communication with limited bandwidth, Topology changes, large no. of sensors
- environmental challenges and application requirements
As well as other networking challenges

## Slide 7: WSNs Applications
Figure 3: WSNs Applications
Notes: These pictures show some of the possible applications of WSNs.
The earliest applications of WSNs were in military field for (surveillance and control).
Later, they’re used for several civilian applications such as:
habitat monitoring
Forest fire detection and air pollution
Underground, seismological, and Volcano Monitoring
Body sensor networks and Several medical applications
they can also be integrated into many smart systems such as “smart cities”: For structural health monitoring, traffic detection, and many other

## Slide 8: Applications of Wireless Sensor networks
The applications can be divided in three categories:
Monitoring of objects.
Monitoring of an area.
Monitoring of both area and objects.

## Slide 9: Monitoring Area
Environmental and Habitat Monitoring
Precision Agriculture
Indoor Climate Control
Military Surveillance
Intelligent Alarms

## Slide 10: Example: Precision Agriculture
Precision agriculture aims at making cultural operations more efficient, while reducing environmental impact.
The information collected from sensors is used to evaluate optimum sowing density, estimate fertilizers and other inputs needs, and to more accurately predict crop yields.

## Slide 11: Monitoring Objects
Structural Monitoring
Eco-physiology
Condition-based Maintenance
Medical Diagnostics
Urban terrain mapping

## Slide 12: Monitoring Interactions between Objects and Space
Wildlife Habitats
Disaster Management
Emergency Response
Ubiquitous Computing
Asset Tracking
Health Care

## Slide 13: Characteristics of Wireless Sensor Networks
Wireless Sensor Networks mainly consists of sensors. Sensors are -
  low power
  limited memory
  energy constrained due to their small size.
Wireless networks can also be deployed in extreme environmental conditions and may be prone to enemy attacks.
Although deployed in an ad hoc manner they need to be self organized and self healing and can face constant reconfiguration.

## Slide 14: Design Challenges
Heterogeneity
  The devices deployed maybe of various types and need to collaborate with each other.
Distributed Processing
  The algorithms need to be centralized as the processing is carried out on different nodes.
Low Bandwidth Communication
  The data should be transferred efficiently between sensors

## Slide 15: Continued..
Large Scale Coordination
  The sensors need to coordinate with each other to produce required results.
Utilization of Sensors
  The sensors should be utilized in a ways that produce the maximum performance and use less energy.
Real Time Computation
  The computation should be done quickly as new data is always being generated.

## Slide 16: Operational Challenges of Wireless Sensor Networks
Energy Efficiency
Limited storage and computation
Low bandwidth and high error rates
Errors are common
  Wireless communication
  Noisy measurements
  Node failure are expected
Scalability to a large number of sensor nodes
Survivability in harsh environments

## Slide 17
Enabling Technologies
Embedded
Networked
Sensing
Control system w/
Small form factor
Untethered nodes
Exploit collaborative
Sensing, action
Tightly coupled to physical world
Embed numerous distributed devices to monitor and interact with physical world
Network devices to coordinate and perform higher-level tasks
Exploit spatially and temporally dense, in situ, sensing and actuation

## Slide 18: Future of WSN Smart Home / Smart Office
Sensors controlling electrical devices in the house.
Better lighting and heating in office buildings.
The Pentagon building has used sensors extensively.

## Slide 19: Biomedical / Medical
Health Monitors
  Glucose
  Heart rate
  Cancer detection
Chronic Diseases
  Artificial retina
  Cochlear implants
Hospital Sensors
  Monitor vital signs
  Record anomalies

## Slide 20: Military
Remote deployment of sensors for tactical monitoring of enemy troop movements.

## Slide 21: Industrial & Commercial
Numerous industrial and commercial applications:
  Agricultural Crop Conditions
  Inventory Tracking
  In-Process Parts Tracking
  Automated Problem Reporting
  Theft Deterrent and Customer Tracing
  Plant Equipment Maintenance Monitoring

## Slide 22: Traffic Management & Monitoring
Future cars could use wireless sensors to:
  Handle Accidents
  Handle Thefts
Sensors embedded in the roads to:
  Monitor traffic flows
  Provide real-time route updates

## Slide 23
Source
www.cse.fau.edu/~jie/teaching/fall_2004_files/sensorslides1.ppt
http://web2.uwindsor.ca/courses/cs/aggarwal/cs60520/SeminarMaterial/WSN-future.ppt
http://web.cecs.pdx.edu/~nbulusu/talks/grace-hopper.ppt
http://galaxy.cs.lamar.edu/~bsun/wsn/wsn.html
www.dsc.ufcg.edu.br/~maspohn/katia/introduction.ppt
http://computer.howstuffworks.com/mote1.htm
http://www.polastre.com/papers/polastre-thesis-final.pdf
References