## Slide 1: Wireless Sensor Networks: A Survey
Arslan Munir
EEL 6935

## Slide 2: Outline
Introduction
Wireless Sensor Networks Applications
Factors Influencing Sensor Network Design
Sensor Node Components
Sensor Networks Communication Architecture
Sensor Network Protocols
Sensor Networks Operating Systems
Sensor Networks Simulators
Conclusion

## Slide 3: Introduction
sensor
  A transducer
  converts physical phenomenon e.g. heat, light, motion, vibration, and sound into electrical signals
sensor node
  basic unit in sensor network
  contains on-board sensors, processor, memory, transceiver, and power supply
sensor network
  consists of a large number of sensor nodes
  nodes deployed either inside or very close to the sensed phenomenon

## Slide 4: Wireless Sensor Networks Applications
Military Applications
Monitoring friendly forces, equipment, and ammunition
Battlefield surveillance
Reconnaissance of opposing forces and terrain
Targeting
Battle damage assessment
Nuclear, biological, and chemical attack detection

## Slide 5: Wireless Sensor Networks Applications
Environmental Applications
Forest fire detection
Bio-complexity mapping of environment
Flood detection
Precision Agriculture
Air and water pollution

## Slide 6: Wireless Sensor Networks Applications
Health Applications
Telemonitoring of human physiological data
Tracking and monitoring doctors and patients inside a hospital
Drug administration in hospitals

## Slide 7: Wireless Sensor Networks Applications
Home and Office Applications
Home and office automation
Smart environment

## Slide 8: Wireless Sensor Networks Applications
Automotive Applications
Reduces wiring effects
Measurements in chambers and rotating parts
Remote technical inspections
Conditions monitoring e.g. at a bearing

## Slide 9: Wireless Sensor Networks Applications
Automotive Applications

## Slide 10: Wireless Sensor Networks Applications
Other Commercial Applications
Environmental control in office buildings (estimated energy savings $55 billion per year!)
Interactive museums
Detecting and monitoring car thefts
Managing inventory control
Vehicle tracking and detection

## Slide 11: Underwater Acoustic Sensor Networks ref. Georgia Institute of Technology

## Slide 12: Factors Influencing WSN Design
Fault tolerance
Scalability
Production costs
Hardware constraints
Sensor network topology
Environment
Transmission media
Power Consumption
  Sensing
  Communication
  Data processing

## Slide 13: Sensor Nodes
Worldsens Inc. Sensor Node
Crossbow Sensor Node

## Slide 14: Sensor Node Components

## Slide 15: Sensor Node Components
Sensing Unit
Processing Unit
Transceiver Unit
Power Unit
Location Finding System (optional)
Power Generator (optional)
Mobilizer (optional)

## Slide 16: WSN Communication Architecture

## Slide 17: WSN Protocol Stack

## Slide 18: A Few WSN Protocols
Sensor management protocol
  Provides software operations needed to perform administrative tasks e.g. moving sensor nodes, turning them on an off
Sensor query and data dissemination protocol
  Provides user applications with interfaces to issue queries and respond to queries
  Sensor query and tasking language (SQTL)
Directed diffusion
Sensor MAC (S-MAC)
IEEE 802.15.4

## Slide 19: Data-Centric Routing
Interest dissemination is performed to assign sensing tasks to sensor nodes
  Sinks broadcast the interest
  Sensor nodes broadcast an advertisement for available data
Requires attribute-based naming
  Users are more interested in querying the attribute of the phenomenon, rather than querying an individual node
  E.g. the sensor nodes in the area where temperature is greater than 75 F

## Slide 20: Data Aggregation in WSNs
Data coming from multiple sensor nodes are aggregated if they are about the same attribute of the phenomenon when they reach the same routing node on the way back to the sink
  Solves implosion and overlap problem
  Energy efficient

## Slide 21: WSN Operating Systems
TinyOS
Contiki
MANTIS
BTnut
SOS
Nano-RK

## Slide 22: TinyOS
Event-driven programming model instead of multithreading
TinyOS and its programs written in nesC
Communication
Actuating
Sensing
Communication
Application (User Components)
Main (includes Scheduler)
Hardware Abstractions

## Slide 23: TinyOS Charactersitics
Small memory footprint
  non-preemptable FIFO task scheduling
Power Efficient
  Puts microcontroller to sleep
  Puts radio to sleep
Concurrency-Intensive Operations
  Event-driven architecture
  Efficient Interrupts and event handling
No Real-time guarantees

## Slide 24: MICA Sensor Mote

## Slide 25: MICA Mote Specifications
4 MHz ATMEGA103L Microprocessor
128 KB of Flash Program Memory
4KB RAM
10 bit Analog to Digital Converter (ADC)
3 Hardware Timers
Serial Peripheral Interface (SPI) bus
External UART
A coprocessor AT90LS2343 (to handle wireless reprogramming)
DS2401 silicon serial number (provides unique ID to nodes)
RF Monolithics TR1000 transceiver
External 4Mbit Atmel AT45DB041B Serial Flash Chip (for persistent data storage)
Maxim1678 DC-DC Converter (provides a constant 3.0 V supply)

## Slide 26: Smart Dust Mote Specifications
4 MHz Atmel AVR 8535 Microprocessor
8 KB Instruction Flash Memory
512 Bytes RAM
512 Bytes EEPROM
Total Stored Energy approx. 1 Joule
TinyOS Operating System (OS) with 3500 bytes OS code space and 4500 bytes available code space

## Slide 27: WSN Development Platforms
Crossbow
Dust Networks
Sensoria Corporation
Ember Corporation
Worldsens

## Slide 28: WSN Simulators
NS-2
GloMoSim
OPNET
SensorSim
J-Sim
OMNeT++
Sidh
SENS

## Slide 29: WSN Emulators
TOSSIM
ATEMU
Avrora
EmStar

## Slide 30: Conclusion
WSNs possible today due to technological advancement in various domains
Envisioned to become an essential part of our lives
Design Constraints need to be satisfied for realization of sensor networks
Tremendous research efforts being made in different layers of WSNs protocol stack

## Slide 31: References
I. F. Akyildiz, W. Su, Y. Sankarasubramaniam, and E. Cayirci, “Wireless Sensor Networks: A Survey”, Elsevier Computer Networks, volume 38, Issue 4, pp. 393-422, March 2002.
Dr. Victor Leung, Lecture Slides on “Wireless Sensor Networks”, University of British Columbia, Canada
D. Curren, “A Survey of Simulation in Sensor Networks”
Wikipedia, [Available Online] http://en.wikipedia.org/wiki/Wireless_Sensor_Networks

## Slide 32: References
Dr. Chenyang Lu Slides on “Berkeley Motes and TinyOS”, Washington University in St. Louis, USA
J. Hill and D. Culler, “A Wireless Embedded Sensor Architecture for System-Level Optimization”, Technical Report, U.C. Berkeley, 2001.
X. Su, B.S. Prabhu, and R. Gadh, “RFID based General Wireless Sensor Interface”, Technical Report, UCLA, 2003.

## Slide 33: Thank you!