Problem :  (5 marks) Bits in  a Cache

- How many total bits are required for a direct-mapped cache with 16KB of data and 16-word blocks, assuming a 32-bit address?

16KB = 4k words, which is 212 words

Block Size 16 words ( 24)   ==> 28 blocks

Each Block has 16×32 = 512 of data

Tag = 32-8-4-2 = 18 bits

Total Cache Size = 28×(512+18+1)=135936

4864 bits overhead

- Show the portions of an address in this mapping

Problem :  (5 marks) Missed and Associativity in Caches

Consider a small cache consisting of a total size of 16 words, configured as direct mapped with one-word blocks. Show the hits and misses and final cache contents given the following sequence of word addresses:    2, 3, 11, 16, 21, 13, 64, 48, 19, 11, 3, 22, 4, 27, 6 , 11

Problem :  (8 marks) Missed and Associativity in Caches

Consider a small cache consisting of a total size of 16 words, configured as direct mapped with four-word blocks. Show the hits and misses and final cache contents given the following sequence of word addresses:    2, 3, 11, 16, 21, 13, 64, 48, 19, 11, 3, 22, 4, 27, 6 , 11

| References | Block # (Memory) | Block # (Cache) | Hit/Miss | 4 words block |
| --- | --- | --- | --- | --- |
| 2 | 0 | 0 | × | 0 1 2 3 |
| 3 | 0 | 0 | ( | 0 1 2 3 |
| 11 | 2 | 2 | × | 8 9 10 11 |
| 16 | 4 | 0 | × | 16 17 18 19 |
| 21 | 5 | 1 | × | 20 21 22 23 |
| 13 | 3 | 3 | × | 12 13 14 15 |
| 64 | 16 | 0 | × | 64 65 66 67 |
| 48 | 12 | 0 | × | 48 49 50 51 |
| 19 | 4 | 0 | × | 16 17 18 19 |
| 11 | 2 | 2 | ( | 8 9 10 11 |
| 3 | 0 | 0 | × | 0 1 2 3 |
| 22 | 5 | 1 | ( | 20 21 22 23 |
| 4 | 1 | 1 | × | 4 5 6 7 |
| 27 | 6 | 2 | × | 24 25 26 27 |
| 6 | 1 | 1 | ( | 4 5 6 7 |
| 11 | 2 | 2 | × | 8 9 10 11 |

Problem :  (8 marks) Missed and Associativity in Caches

Repeat the above Problem if it is:

Two-way set associative with one-word blocks (assume LRU replacement) given the following sequence of word addresses:    2, 3, 11, 16, 21, 13, 64, 48, 19, 11, 3, 22, 4, 27, 6 , 11

Problem 4:  (8 marks) Bits in  a Cache

For a cache of 16k blocks, a four-word block size, and a 32-bit address. Find the total number of sets and the total number of tag bits for caches that are: direct mapped, two-way and four-way set associative, and fully associative.

| Cache | Total number of sets | Total number of tag bits |
| --- | --- | --- |
| Direct-Mapped | 214 | 224 kbits |
| Two-way set-associative | 213 | 240 kbits |
| Four-way set-associative | 212 | 256 kbits |
| Fully associative | 1 | 448 kbits |

Direct mapped:

214 Blocks

22 Words/Block

Tag bits = 32-14-2-2 =14

Total # of sets = 214 sets

Total # of Tag bits = 14×214 = 14×24×210 bits = 224 kbits

Two-way-set-associative:

213 sets

22 Words/Block

Tag bits = 32-13-2-2 =15

Total # of sets = 213 sets

Total # of Tag bits = 15×2×213 = 15×24×210 bits = 240 kbits

# Text boxes

| 0 | 0 | 0 | 1 | 2 | 3 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 4 | 5 | 6 | 7 |
| 2 | 2 | 8 | 9 | 10 | 11 |
| 3 | 3 | 12 | 13 | 14 | 15 |
| 0 | 4 | 16 | 17 | 18 | 19 |
| 1 | 5 | 20 | 21 | 22 | 23 |
| 2 | 6 | 24 | 25 | 26 | 27 |
| 3 | 7 | 28 | 29 | 30 | 31 |
| 0 | 8 | 32 | 33 | 34 | 35 |
| 1 | 9 | 36 | 37 | 38 | 39 |
| 2 | 10 | 40 | 41 | 42 | 43 |
| 3 | 11 | 44 | 45 | 46 | 47 |
| 0 | 12 | 48 | 49 | 50 | 51 |
| 1 | 13 | 52 | 53 | 54 | 55 |
| 2 | 14 | 56 | 57 | 58 | 59 |
| 3 | 15 | 60 | 61 | 62 | 63 |
| 0 | 16 | 64 | 65 | 66 | 67 |